## Slide 1: High Rate Machine Learning for Forecasting Time-Series Signals
Atiyehsadat Panahi
Ehsan Kabir
David Andrews
Miaoqing Huang
Jason D. Bakos
Heterogeneous and Reconfigurable Computing Group
This material is based upon work supported by the National Science Foundation under Grant No. 1956071.
Austin Downey

## Slide 2: Objectives
current time
future time
(predict this)
Objective:
Simultaneous forecast +
learn for time series
Performance metrics:
Forecast accuracy
Re-training time
Latency
Contributions:
Algorithms
HLS-based implementation
Overlay-based implementation

## Slide 3: Time Series Forecasting
current time
time
forecast time (f)
forecast
Most recent sample
error

## Slide 4: Applications: Control of Active Structures
Active Vibration Control
Deformable Mirrors
Sensors
Structure
Actuator
Control System
* ALPAO Corp.

## Slide 5: Approach
Signal must be periodic
Period unknown and may be too long for timely relearn
Nonstationarity

## Slide 6: Approach: MLP-Based Model
current time
time
backward pass
forward pass
history length (h)
history length (h)
forecast time (f)
forecast time (f)
MLP1
MLP2

## Slide 7: Test Data
stimulus:
100 Hz+120 Hz+150 Hz
stimulus:
100 Hz+120 Hz
nonstationarity
???

## Slide 8: System Design
z-1
z-1
z-1
z-1
z-1
z-1
t : t-h-1
t-f : t-f-h-1
forecast
learn
…
…
…
rate r to rate rs
word size n
51.2 KHz
rs Hz
execution time < 1/rs

## Slide 9: Performance Metrics
Forecast accuracy:
Re-training time:
  Fit absolute error to
  Find "center of gravity" of curve:
Parameters:
  History length (h)
  Hidden layer size (s)
  Subsample rate (rs)
  Data width (n)

## Slide 10: Impact of h, s, rs, and n on Accuracy
Subsampled @ 2500 Hz
Subsampled @ 2500 Hz
50 hidden neurons

## Slide 11: Impact of h, s, rs, and n on Retraining Time
Subsampled @ 2500 Hz
Subsampled @ 2500 Hz
50 hidden neurons

## Slide 12: Deployment Results

## Slide 13: HLS Architecture
Vivado HLS 2019.1
Pipelined loops (hidden layer):
  Forward pass 1 (forecast)
  Forward pass 2 (loss calculation)
    Latency = cycles
      h = history length
      s = hidden layer size
    IL = ~2*h (for > 400MHz)
  Hidden layer weight update
    Latency = cycles
    IL = ~1 - 7 cycles
serial/parallel converter
forward pass 1
cycles
forward pass 2
cycles
hidden layer gradient calculation
output neuron weight update
hidden layer weight update
cycles
complete unroll
complete unroll
complete unroll
Steps:

## Slide 14: HLS Implementation
Targeted Virtex Ultrascale+ VU9P
  484 MHz
Has fixed BRAM/DSP usage for 1024-banks
  1 MB allocated weight capacity
  Largest model uses only 15% of allocated RAM
Current design limited by LUT usage
uses 15% of allocated BRAM
320K parameters
20K parameters

## Slide 15: Array Processor Memory
SPAR-2 processor
  2D array of 1-bit PEs
  Latencies (8-bit):
    add = 16 cycles
    mult = 80 cycles
    n-way reduction =8 cycles
  4x4 block of PEs associated with one BRAM
A. Panahi, S. Balsalama, A. T. Ishimwe, J.M. Mbongue, D. Andrews,
"A Customizable Domain-Specific Memory-Centric FPGA Overlay for Machine Learning Applications," FPL 2021.

## Slide 16: Array Processor Architecture
Structure:
  5x5 blocks/tile
  5x5 tiles/grid
  10K PEs
PEs can exchange with neighbors
10 MB capacity, best performance when weights < 160 KB
Custom instructions added for backpropagatation
vs HLS:
  Overcomes HLS's 1024-bank limit
  Limited by multi-cycle adds and lower Fmax of 330 MHz

## Slide 17: Performance Results

## Slide 18: Conclusions
Real-time, data driven simultaneous forecasting and learning of time series signals
Developed two implementations of the system
Current work:
  Dynamically adjust learning rate to improve re-training time
  Add support for LSTM forecasters

## Slide 19: Thank you!