## Slide 1: Lucas Kanade Optical Flow Estimation on the TI C66x Digital Signal Processor
Fan Zhang, Yang Gao and Jason D. Bakos
2014 IEEE High Performance Extreme Computing Conference(HPEC ‘14)

## Slide 2: What is Optical Flow
Evaluates the pixel movement in video stream
  Represented as a dense 2D fields
Many applications need to apply real-time optical flow
  Robotic vision
  Augmented reality
Computationally intensive

## Slide 3: TI C66x Multicore DSP
Unique architectural features
  Eight cores
  Statically scheduled VLIW/SIMD instructions
  2 register files and 8 functional units per core
 | Tesla K20X GPU | Intel i7 Ivy Bridge | TI C6678 Keystone | NVIDIA Tegra K1
 | Server GPU | Server CPU | Embedded | Embedded
Peak single precision throughput | 3.95 Tflops | 448 Gflops | 160 Gflops | 327 Gflops
Peak Power | 225 W | 77 W | <10 W | <20 W
DRAM bandwidth | 250 GB/s | 25.6 GB/s | 12.8 GB/s | 17.1 GB/s

## Slide 4: Why using DSP?
Low power consumption
High performance floating point arithmetic
Strong potential for computer vision tasks
  1D vs 2D (signal processing vs image processing)

## Slide 5: Gradient-based Optical Flow Solver
Optical flow evaluation
First-order approximation
One formula with two unknowns
Gradient of pixel in x, y and t direction, known
Optical flow, unknown
.
.
(x, y, t)
(x + Δx, y + Δ y, t + Δt)
Frame t
Frame t + Δt

## Slide 6: Lucas Kanade Method
x-1,y-1 | x,y-1 | x+1,y-1
x-1,y | x,y | x+1,y
x-1,y+1 | x,y+1 | x+1,y+1
If we assume the pixel adjacent to the center has the same optical flow as the center
Let
Least Square Method

## Slide 7: Image Derivative Computation
7
frame n
frame n
frame n
frame n+1
(A – B + C – D) / 2
B
D
A
C
B
D
A
C
(A – C + B – D) / 2
A
B
A - B

## Slide 8: Lucas Kanade Method
Input: Frame n, frame n+1, window size w
Output: Optical flow field F
For each pixel x, y
Compute x,y,t derivative matrices Dx, Dy, Dt
for its neighbor window
Compute optical flow by the least square
method

## Slide 9: Derivative Computation (Example)
10 | 10 | 10 | 10
10 | 30 | 10 | 10
10 | 10 | 10 | 10
10 | 10 | 10 | 10
10 | 10 | 10 | 10
10 | 10 | 10 | 10
10 | 10 | 30 | 10
10 | 10 | 10 | 10
-10 | 10 | 0
-10 | 10 | 0
0 | 0 | 0
-10 | -10 | 0
10 | 10 | 0
0 | 0 | 0
Image n
Image n + 1
0 | 0 | 0
0 | 20 | 0
0 | 0 | -20

## Slide 10: Least Square Method Example (Neighbor Window Size = 3)
-10 | 10 | 0
-10 | 10 | 0
0 | 0 | 0
-10 | -10 | 0
10 | 10 | 0
0 | 0 | 0
0 | 0 | 0
0 | 20 | 0
0 | 0 | -20

## Slide 11: Optimize Lucas Kanade Method on DSP
Derivative computation
  SIMD arithmetic
  Data interleaving
Least square method
  Loop unrolling
  SIMD load & arithmetic

## Slide 12: Derivative Computation
10 | 10 | 10 | 10
10 | 30 | 10 | 10
10 | 10 | 10 | 10
10 | 10 | 10 | 10
-10 | 10 | 0
-10 | 10 | 0
0 | 0 | 0
-10 | -10 | 0
10 | 10 | 0
0 | 0 | 0
Derivative Computation (Dx, Dy)
Interleave
-10 | -10 | 10 | -10 | 0 | 0
-10 | 10 | 10 | 10 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0
Cycle 1
Cycle 2
Cycle 3

## Slide 13: Least Square Method
Required computations
Dx
Dy
Dt
DxDx
DxDy
DyDy
DxDt
DyDt
Multiplication x 5
Accumulation x 5
Map to device
Dx
Dy
Dt
Dt
Complex Mul
2-way SIMD Mul
DxDy
-DyDy
(a+bj)(c+dj) = (ac-bd) + (ad+bc)j
DyDx
DxDx
DxDt
DyDt

## Slide 14: Least Square Method
Unrolled 2x
  Group up loads into SIMD operation
0 | 0 | 0
0 | 20 | 0
0 | 0 | -20
-10 | -10 | 10 | -10 | 0 | 0
-10 | 10 | 10 | 10 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0
(Dx,Dy,Dt)
-10 | -10 | 0
10 | -10 | 0
(Dx,Dy,Dt)
(DxDx,DxDy,DyDy,DxDt,DyDt)
100 | 100 | 100 | 0 | 0
(DxDx,DxDy,DyDy,DxDt,DyDt)
100 | -100 | 100 | 0 | 0
+
200
0
200
0
0
-10
-10
10
-10
0
0
100
100
100
0
0
100
-100
100
0
0
200
0
200
0
0
Load DxDy
Load Dt
Complex MUL
SIMD MUL
SIMD ADD
DxDy
Dt

## Slide 15: Loop Flattening
Software Pipelining
  TI’s compiler technique to allow independent loop iterations be executed in parallel
  The consecutive iterations are packed and executed together so that the arithmetic functional units are fully utilized
for (i = 0; i < m; ++i)
for (j = 0; j < n; ++j)
j = 0
j = 1
for (k = 0; k < m * n; ++k)
…
Update i, j;
Pipeline prologue/epilogue overhead
j = 0
j = 1

## Slide 16: Multicore Utilization
Derivative Computation
Least Square Method
Least Square Method
Least Square Method
Core 0
Core 1
Core 2
…
…
Row [0, k)
Row [k, 2k)
Row [2k, 3k)
Cache sync
k = numRows / numCores

## Slide 17: Accuracy Improvement
Cannot catch movement larger than window size
  Gaussian Pyramid
    A coarse to fine strategy for optical flow computation
    Catches large movements
First order approximation may not be accurate
  Iterative refinement
    Iteratively process and offset pixels until the computed optical flow is converged
    Introduce data random access

## Slide 18: Experiment Setup
Platform | #Cores | Implementation | Power Measurement
TI C6678 DSP | 8 | Our Implementation | TI GPIO-USB Module
ARM Cortex A9 | 2 | Our Implementation | YOKOGAWA WT500 Power Analyzer
Intel i7-2600 | 4 | Our Implementation | Intel RAPL
Tesla K20 GPU | 2688 | OpenCV | NVIDIA SMI

## Slide 19: Results and Analysis
Highest Performance
  Tesla K20
Lowest Power
  Cortex A9
Best Power Efficiency
  TI C66x DSP
Platform | C66x | CortexA9 | Intel i7-2600 | K20
Actual Gflops/ Peak Gflops | 12% | 7% | 4% | 3%
Gflops | 15.4 | 0.7 | 17.1 | 108.6
Power (W) | 5.7 | 4.8 | 52.5 | 79.0
Gflops/W | 2.69 | 0.2 | 0.3 | 1.4

## Slide 20: Results and Analysis
We achieve linear scalability on multi-cores
The power efficiency of the DSP is low when its cores are partially utilized
  Static power consumption

## Slide 21: Results and Analysis
Performance are related with window size
  Software pipeline performance
Loop flattening is able to improve performance significantly on small window size

## Slide 22: Conclusion
First research work on DPS accelerated Lucas Kanade method
Achieve higher energy efficiency and device utilization than GPU and CPU

## Slide 23: Q & A

## Slide 24: Kernels of Pyramidal Lucas Kanade Method
Gaussian Blur
Derivative Computation
Least Square Method
Flow Field Bilinear Interpolation
Window Size = 16, Pyramid Level = 4, Iteration = 10
105 flop/pixel
3 flop/pixel
8 flop/pixel
28 flop/pixel