## Slide 1
Fundamentals of P4 and DPDK
Elie Kfoury, Jorge Crichigno
University of South Carolina (USC)
https://research.cec.sc.edu/cyberinfra
University of South Carolina (USC)
The Engagement and Performance Operations Center (EPOC)
Minority Serving - Cyberinfrastructure Consortium (MS-CC)
Hands-on Workshop on Science DMZ and P4-DPDK
Thursday, April 17, 2025.

## Slide 2: Agenda
Overview on packet processing
Kernel-bypass (DPDK)
P4 language
Programming DPDK with P4
Advances in Network Interface Cards
Security applications offload to next-generation NICs
Conclusion

## Slide 3
Packet Processing on End Hosts

## Slide 4: Packet Processing
The Network Interface Card (NIC) driver pre-allocates kernel memory buffers where the packets are stored
Application
Kernel space
User space
  Rinku Shah and Priyanka Naik, Kernel-bypass techniques for high-speed network packet processing. https://tinyurl.com/3bzfehja
NIC driver
Packet buffer
Packet buffer
Packet buffer
…
Packet buffer
Memory buffers

## Slide 5: Packet Processing
The Network Interface Card (NIC) driver pre-allocates kernel memory buffers where the packets are stored
The NIC driver pre-allocate the transmit (TX) and receive (RX) ring buffer in the memory
NIC
Application
Kernel space
User space
TX
RX
NIC driver
Packet buffer
Packet buffer
Packet buffer
…
Packet buffer
Memory buffers
  Rinku Shah and Priyanka Naik, Kernel-bypass techniques for high-speed network packet processing. https://tinyurl.com/3bzfehja

## Slide 6: Packet Processing
NIC
Application
Kernel space
User space
TX
RX
NIC driver
Packet buffer
Packet buffer
Packet buffer
…
Packet buffer
Memory buffers
The Network Interface Card (NIC) driver pre-allocates kernel memory buffers where the packets are stored
The NIC driver pre-allocate the transmit (TX) and receive (RX) ring buffer in the memory
The ring buffers store the packet buffer pointer and its length
  Rinku Shah and Priyanka Naik, Kernel-bypass techniques for high-speed network packet processing. https://tinyurl.com/3bzfehja
Notes: The NIC driver pre-allocates kernel memory buffers where the packets are stored
The NIC driver pre-allocate the transmit (TX) and receive (RX) ring buffer in the memory
The ring buffers are circular queues shared between the NIC and the driver
The ring buffers store the packet buffer pointer and its length

## Slide 7: Packet Processing
The Network Interface Card (NIC) driver pre-allocates kernel memory buffers where the packets are stored
The NIC driver pre-allocate the transmit (TX) and receive (RX) ring buffer in the memory
The ring buffers store the packet buffer pointer and its length
The NIC copies the packet to the location using Direct Memory Access (DMA)
NIC
Application
Kernel space
User space
TX
RX
NIC driver
Packet buffer
Packet buffer
…
Packet buffer
Hardware RX queue
Memory buffers
  Rinku Shah and Priyanka Naik, Kernel-bypass techniques for high-speed network packet processing. https://tinyurl.com/3bzfehja

## Slide 8: Packet Processing
The Network Interface Card (NIC) driver pre-allocates kernel memory buffers where the packets are stored
The NIC driver pre-allocate the transmit (TX) and receive (RX) ring buffer in the memory
The ring buffers store the packet buffer pointer and its length
The NIC copies the packet to the location using Direct Memory Access (DMA)
The NIC triggers an interrupt
NIC
Application
Kernel space
User space
TX
RX
NIC driver
Packet buffer
Packet buffer
…
Packet buffer
Hardware RX queue
Memory buffers
  Rinku Shah and Priyanka Naik, Kernel-bypass techniques for high-speed network packet processing. https://tinyurl.com/3bzfehja

## Slide 9: Packet Processing
Interrupt processing:
The CPU pauses the process in execution
  Rinku Shah and Priyanka Naik, Kernel-bypass techniques for high-speed network packet processing. https://tinyurl.com/3bzfehja

## Slide 10: Packet Processing
Interrupt processing:
The CPU pauses the process in execution
Switch from user space to kernel space
  Rinku Shah and Priyanka Naik, Kernel-bypass techniques for high-speed network packet processing. https://tinyurl.com/3bzfehja

## Slide 11: Packet Processing
Interrupt processing:
The CPU pauses the process in execution
Switch from user space to kernel space
Acknowledge of schedule bottom-half processing
  Rinku Shah and Priyanka Naik, Kernel-bypass techniques for high-speed network packet processing. https://tinyurl.com/3bzfehja

## Slide 12: Packet Processing
Interrupt processing:
The CPU pauses the process in execution
Switch from user space to kernel space
Acknowledge of schedule bottom-half processing
Switch back to user space
  Rinku Shah and Priyanka Naik, Kernel-bypass techniques for high-speed network packet processing. https://tinyurl.com/3bzfehja

## Slide 13: Packet Processing
Interrupt processing:
The CPU initiates the bottom-half when it is free
Switch from user space to kernel space
  Rinku Shah and Priyanka Naik, Kernel-bypass techniques for high-speed network packet processing. https://tinyurl.com/3bzfehja

## Slide 14: Packet Processing
Interrupt processing:
The CPU initiates the bottom-half when it is free
Switch from user space to kernel space
Dynamically allocate packet data structure
Remove Ethernet header and pass to network stack
  Rinku Shah and Priyanka Naik, Kernel-bypass techniques for high-speed network packet processing. https://tinyurl.com/3bzfehja

## Slide 15: Packet Processing
Interrupt processing:
The CPU initiates the bottom-half when it is free
Switch from user space to kernel space
Dynamically allocate packet data structure
Remove Ethernet header and pass to network stack
For all packets in buffer
  Rinku Shah and Priyanka Naik, Kernel-bypass techniques for high-speed network packet processing. https://tinyurl.com/3bzfehja

## Slide 16: Packet Processing Overheads
Too many context switches, polluting CPU cache
Per-packet interrupt overhead
Dynamic allocation of packet data structure
Packet copy between the kernel and user space
  Rinku Shah and Priyanka Naik, Kernel-bypass techniques for high-speed network packet processing. https://tinyurl.com/3bzfehja

## Slide 17: Packet Processing Overheads
Too many context switches, polluting CPU cache
Per-packet interrupt overhead
Dynamic allocation of packet data structure
Packet copy between the kernel and user space
Link Capacity | Packet Size | Time Budget per Packet
10 Mbps | 64 bytes | 51,200 ns
100 Mbps | 64 bytes | 5,120 ns
1 Gbps | 64 bytes | 512 ns
10 Gbps | 64 bytes | 51.2 ns
100 Gbps | 64 bytes | 5.12 ns
  Rinku Shah and Priyanka Naik, Kernel-bypass techniques for high-speed network packet processing. https://tinyurl.com/3bzfehja

## Slide 18: Kernel-bypass
One approach to avoid the overhead is to bypass the kernel
DPDK is a set of optimized libraries for processing packets in the user space
DPDK bypasses the kernel
DPDK uses Poll Mode Drivers (PMD) which constantly poll the NICs for new packets
This avoids the overheads resulting from interrupts
DPDK-supported NIC
Application
Kernel space
User space
DPDK Poll Mode Driver (PMD)
DPDK: Data Plane Development Kit

## Slide 19: Multicore CPUs
DPDK enables packet processing on multicore CPUs
The Receive Side Scaling (RSS) technique is used to distribute the packets to the CPU cores
The CPU cores can run different packet processing pipelines

## Slide 20: DPDK Performance
Layer-3 forwarding (l3fwd) is implemented in DPDK1
100Gbps line rate for 64 bytes packets
1NVIDIA NICs Performance Report with DPDK 23.11. https://fast.dpdk.org/doc/perf/DPDK_23_11_NVIDIA_NIC_performance_report.pdf

## Slide 21: DPDK Challenges
DPDK is complex and required deep understanding of C and DPDK libraries
DPDK requires millions of lines of code in C to implement a software switch
Difficult to add new features to the large code

## Slide 22: P4 Language
P4 emerged as domain-specific language to define packet processing:
  Define and parse new protocols
  Customize packet processing functions

## Slide 23
Match+Action Stage
Memory
ALU
Programmable Parser
Programmable Match-Action Pipeline
PISA: Protocol Independent Switch Architecture
N. McKeown. Creating an End-to-End Programming Model for Packet Forwarding. Available: https://www.youtube.com/watch?v=fiBuao6YZl0&t=4216s

## Slide 24
PISA: Protocol Independent Switch Architecture
24
N. McKeown. Creating an End-to-End Programming Model for Packet Forwarding. Available: https://www.youtube.com/watch?v=fiBuao6YZl0&t=4216s

## Slide 25: Example P4 Program
Memory
ALU
Programmable Parser
Programmable Match-Action Pipeline
header_type ethernet_t { … }
header_type l2_metadata_t { … }
header ethernet_t ethernet;
header vlan_tag_t vlan_tag[2];
metadata l2_metadata_t l2_meta;
Header and Data Declarations
Parser Program
parser parse_ethernet { extract(ethernet); return switch(ethernet.ethertype) { 0x8100 : parse_vlan_tag; 0x0800 : parse_ipv4; 0x8847 : parse_mpls; default: ingress; }
Tables and Control Flow
table port_table { … }
control ingress { apply(port_table); if (l2_meta.vlan_tags == 0) { process_assign_vlan();
} }
25
N. McKeown. Creating an End-to-End Programming Model for Packet Forwarding. Available: https://www.youtube.com/watch?v=fiBuao6YZl0&t=4216s

## Slide 26: Why P4 for CPU?
Processing packets on the server is very similar to a switch pipeline
  Packets need to be parsed
  Match and action operations are performed on the packets
  Packets are sent to the network or the host
Memory
ALU
Programmable Parser
Programmable Match-Action Pipeline
Programmable Deparser

## Slide 27: Why P4 for CPU?
The P4 description for a data plane is short
For example, a full implementation of a data center switch requires1:
  ~5000 lines of code in P4
  Millions of lines of code in C with DPDK
  1Running P4 programs as DPDK applications - Cristian Dumitrescu & Han Wang – Intel. https://www.youtube.com/watch?v=xJR-5DcqhlY
Attack | DPDK | P4
DNS amplification | 898 | 255
HTTP flood | 1184 | 354
SlowLoris | 995 | 513
UDP flood | 911 | 376
Elephant flow (heavy hitter) | 903 | 373
Lines of code (LOC) for implementing defenses against common cyberattacks1

## Slide 28: Why P4 for CPU?
DPDK is complex and required deep understanding of C and DPDK libraries
P4’s high-level abstraction simplifies the development of complex packet processing
P4 quickly adapts and deploys new network functions to the data plane

## Slide 29: Why P4 for CPU?
DPDK is complex and required deep understanding of C and DPDK libraries
P4’s high-level abstraction simplifies the development of complex packet processing
P4 quickly adapts and deploys new network functions to the data plane
Combining P4 with DPDK enables highly customizable, high-performance network applications that benefit from both the programmability of P4 and the efficiency of DPDK

## Slide 30: P4-DPDK
P4-DPDK is an initiative that translates P4 code to DPDK

## Slide 31: P4-DPDK Supported Features
  Do not develop from scratch, simply write P4 and get DPDK - Cristian Dumitrescu, Intel. https://tinyurl.com/38574yh9

## Slide 32: P4 Across the Network Stack
P4 has been used in targets other than switches:
  SmartNICs: NICs with a programmable pipeline implemented in FPGA, ASIC, or SoC
  Virtual switches: software switches used to connect virtual networks such as Open vSwitch (OvS)
  End hosts stacks: User space and kernel space

## Slide 33: P4 Across the Network Stack
P4 has been used in targets other than switches:
  SmartNICs: NICs with a programmable pipeline implemented in FPGA, ASIC, or SoC
  Virtual switches: software switches used to connect virtual networks such as Open vSwitch (OvS)
  End hosts stacks: User space and kernel space
The vision is to create an end-to-end programmable network
  N. McKeown, The Network will be programmed by many, operated by a few. The Networking Channel: https://tinyurl.com/3wukc8zn

## Slide 34: Conclusion
The packet processing stack on the server has overheads due to context switching, interrupts, packet copy, etc.
DPDK minimize the overhead by bypassing the kernel
DPDK can leverage multicore CPU to enhance the packet processing performance
P4-DPDK combines the expressiveness of P4 and the performance of DPDK
A shared vision in the community is to create a fully programmable stack including switches, servers, and NICs