## Slide 1
National Science Foundation Award #1826994
Designing, Building, & Maintaining
a Science DMZ and Data Architecture
Modern Cyberinfrastructure for Research Data Management Workshop
University of Central Florida
February 16-17, 2023
https://epoc.global
Ken Miller, Jason Zurawski
ken@es.net, zurawski@es.net
ESnet / Lawrence Berkeley National Laboratory

## Slide 2: Outline
Introduction
Solution Space
Putting it Together
Conclusions / QA

## Slide 3: Measurable Outcomes
How to prepare for research use of technology on a campus?
  “Build CI” – but is this all?
  Improve scientific outcomes in some measurable way
Things to consider (pre, during, post):
  Has it/will it all work as expected? (e.g. more than plugging in wires)
  Will we all be satisfied at the end? (researchers are the survey population, not just the IT org …)
  How do you know when you/we are done? Are you ever done?
Think of this set of content as a reset – we don’t want to build IT for the sake of building IT
  Tie things back to the user/use cases, and be sensible about the design, installation, and operation

## Slide 4
Network as Infrastructure Instrument
Connectivity is the first step – usability must follow

## Slide 5: Where do we go from here?
WHO and WHY are the most important questions
  Know the users, know the use cases. Those will guide any technical solution
WHAT and HOW go together:
  Figuring out the technology that will help without causing non-productive disruptions
  Being able to sensibly design, implement, and operate
  We have to address item 1, then we will dive into item 2

## Slide 6: Outline
Introduction
Solution Space
  Understanding the Solution Space (Users, Use Cases, Long Term Impacts)
  Preliminaries (e.g. Network Protocols 101)
  Architecture & Design
  Monitoring and Measurement
  Data Mobility
  Security and Policy
Putting it Together
Conclusions / QA

## Slide 7: Common Theme / New Mindset
We aren’t building a “Network Architecture”, we want a “Data Architecture”
  A lot of the items that will be thrown at you transcend the traditional network space.
To get there:
  Understand the data pipeline for your target user/use case – cradle to retirement home
  This implies all the things:
    Creation
    Usage
    Transfer/Share
    Curation

## Slide 8: Common Theme / New Mindset
What you build must be
  Usable – if this becomes a ‘walled garden’, what’s the point? Make it such that people can be easily onboarded and integrated.
  Defensible – it is not, nor should it be, the wild west. Control the users and use cases, but don’t impact the usage.
  Scalable – as demand grows. Think cornfields and baseball diamonds.
  an institutional capability / source of pride – this is something that will draw more users / research dollars if created/marketed/operated correctly. Treat it as such.

## Slide 9: Outline
Introduction
Solution Space
  Understanding the Solution Space (Users, Use Cases, Long Term Impacts)
  Preliminaries (e.g. Network Protocols 101)
  Architecture & Design
  Monitoring and Measurement
  Data Mobility
  Security and Policy
Putting it Together
Conclusions / QA

## Slide 10: Data Movement / TCP Background
The data mobility performance requirements for data intensive science are beyond what can typically be achieved using traditional methods
  Default host configurations (TCP, filesystems, NICs)
  Converged network architectures designed for commodity traffic
  Conventional security tools and policies
  Legacy data transfer tools (e.g. SCP, FTP)
  Wait-for-trouble-ticket operational models for network performance
Notes: The Science DMZ model is a set of ideas – the diagrams that follow are examples.

## Slide 11: TCP – Ubiquitous and Fragile
Networks provide connectivity between hosts – how do hosts see the network?
  From an application’s perspective, the interface to “the other end” is a socket
  Communication is between applications – mostly over TCP
  Congestion dictates performance – back off when danger is sensed to preserve/protect resources
TCP – the fragile workhorse
  TCP is (for very good reasons) timid – packet loss is interpreted as congestion
  Packet loss in conjunction with latency is a performance killer
  Like it or not, TCP is used for the vast majority of data transfer applications (more than 95% of ESnet traffic is TCP)

## Slide 12: A small amount of packet loss makes a huge difference in TCP performance
Metro Area
Local
(LAN)
Regional
Continental
International
Measured (TCP Reno)
Measured (HTCP)
Theoretical (TCP Reno)
Measured (no loss)
With loss, high performance beyond metro distances is essentially impossible
Notes: On a 10 Gb/s LAN path the impact of low packet loss rates is minimal
On a 10 Gb/s WAN path the impact of low packet loss rates is enormous
Beyond your metro area, zero loss is essentially required for performance
Where are your collaborators? Where are your users?
When global collaboration is the norm, nobody can afford to be a local-only resource

## Slide 13: Data Movement / TCP Background
The Science DMZ model describes a performance-based approach
  Dedicated infrastructure for wide-area data transfer
    Well-configured data transfer hosts with modern tools
    Capable network devices
    High-performance data path which does not traverse commodity LAN
  Proactive operational models that enable performance
    Well-deployed test and measurement tools (perfSONAR)
    Periodic testing to locate issues instead of waiting for users to complain
  Security posture well-matched to high-performance science applications
Notes: The Science DMZ model is a set of ideas – the diagrams that follow are examples.

## Slide 14: The Science DMZ in 1 Slide
Consists of four key components, all required:
“Friction free” network path
  Highly capable network devices (wire-speed, deep queues)
  Virtual circuit connectivity option
  Security policy and enforcement specific to science workflows
  Located at or near site perimeter if possible
Dedicated, high-performance Data Transfer Nodes (DTNs)
  Hardware, operating system, libraries all optimized for transfer
  Includes optimized data transfer tools such as Globus Online and GridFTP
Performance measurement/test node
  perfSONAR
Engagement with end users
  Details at http://fasterdata.es.net/science-dmz/
© 2013 Wikipedia

## Slide 15: Outline
Introduction
Solution Space
  Understanding the Solution Space (Users, Use Cases, Long Term Impacts)
  Preliminaries (e.g. Network Protocols 101)
  Architecture & Design
  Monitoring and Measurement
  Data Mobility
  Security and Policy
Putting it Together
Conclusions / QA

## Slide 16: Science DMZ Takes Many Forms
There are a lot of ways to combine these things – it all depends on what you need to do
  Small installation for a project or two
  Facility inside a larger institution
  Institutional capability serving multiple departments/divisions
  Science capability that consumes a majority of the infrastructure
Some of these are straightforward, others are less obvious
Key point of concentration: eliminate sources of packet loss / packet friction

## Slide 17: Legacy Method: Ad Hoc DTN Deployment
This is often what gets tried first
Data transfer node deployed where the owner has space
  This is often the easiest thing to do at the time
  Straightforward to turn on, hard to achieve performance
If lucky, perfSONAR is at the border
  This is a good start
  Need a second one next to the DTN
Entire LAN path has to be sized for data flows
Entire LAN path is part of any troubleshooting exercise
This usually fails to provide the necessary performance.
Notes: Previous slide is diagram for this; just say these things while showing previous slide

## Slide 18: Ad Hoc DTN Deployment
Notes: DTN node deep within campus infrastructure.

## Slide 19: A better approach: simple Science DMZ
Notes: Add-on to existing network infrastructure
  All that is required is a port on the border router
  Small footprint, pre-production commitment
Easy to experiment with components and technologies
  DTN prototyping
  perfSONAR testing
Limited scope makes security policy exceptions easy
  Only allow traffic from partners
  Add-on to production infrastructure – lower risk

## Slide 20: Distributed Science DMZ – Dark Fiber

## Slide 21: Multiple Science DMZs – Dark Fiber to Dedicated Switches

## Slide 22: Design Thoughts – E.g. where does the capability live?
There are two main schools of thought when going after the CC* design area:
  Create an enclave for the science use cases designed specifically to facilitate them. Move things in 1:1
  Drop in replacement of a network such that we can capture a bunch of use cases with a big net (and not dig in too deeply)
A strong proposal adopts a stance closer to 1 – its important to know use cases. Its also important to justify expense of equipment to a need
Number 2 is easier to accomplish (e.g. design, potentially to operate) since its just a ’bigger/better’ network that could lift all boats.

## Slide 23: Equipment – Routers and Switches
Requirements for Science DMZ gear are different than the enterprise
  No need to go for the kitchen sink list of services
  A Science DMZ box only needs to do a few things, but do them well
  Support for the latest LAN integration magic with your Windows Active Directory environment is probably not super-important
  A clean architecture is important
    How fast can a single flow go?
    Are there any components that go slower than interface wire speed?
There is a temptation to go cheap
  Hey, it only needs to do a few things, right?
  You typically don’t get what you don’t pay for
    (You sometimes don’t get what you pay for either)

## Slide 24: Common Circumstance: Multiple Ingress Data Flows, Common Egress
Hosts will typically send packets at the speed of their interface (1G, 10G, etc.)
  Instantaneous rate, not average rate
  If TCP has window available and data to send, host sends until there is either no data or no window
Hosts moving big data (e.g. DTNs) can send large bursts of back-to-back packets
  This is true even if the average rate as measured over seconds is slower (e.g. 4Gbps)
  On microsecond time scales, there is often congestion
  Router or switch must queue packets or drop them

## Slide 25: Some Stuff We Think Is Important
Deep interface queues (e.g. buffer)
  Output queue or VOQ – doesn’t matter
  What TCP sees is what matters – fan-in is *not* your friend
  No, this isn’t buffer bloat
Good counters
  We like the ability to reliably count *every* packet associated with a particular flow, address pair, etc
    Very helpful for debugging packet loss
    Must not affect performance (just count it, don’t punt it)
    sflow support if possible
  If the box is going to drop a packet, it should increment a counter somewhere indicating that it dropped the packet
    Magic vendor permissions and hidden commands should not be necessary
    Some boxes just lie – run away!
Single-flow performance should be wire-speed

## Slide 26: All About That Buffer (No Cut Through)

## Slide 27: All About That Buffer (No Cut Through)
Data arrives from multiple sources
Buffers have a finite amount of memory
  Some have this per interface
  Others may have access to a shared memory region with other interfaces
The processing engine will:
  Extract each packet/frame from the queues
  Pull off header information to see where the destination should be
  Move the packet/frame to the correct output queue
Additional delay is possible as the queues physically write the packet to the transport medium (e.g. optical interface, copper interface)

## Slide 28: All About That Buffer (No Cut Through)
The Bandwidth Delay Product
  The amount of “in flight” data for a TCP connection (BDP = bandwidth * round trip time)
Example: 10Gb/s cross country, ~100ms
  10,000,000,000 b/s * .1 s = 1,000,000,000 bits
  1,000,000,000 / 8 = 125,000,000 bytes
  125,000,000 bytes / (1024*1024) ~ 125MB
Ignore the math aspect: its making sure there is memory to catch and send packets
  At ALL hops
  As the speed increases, there are more packets.
  If there is not memory, we drop them, and that makes TCP react, and the user sad.

## Slide 29: All About That Buffer (No Cut Through)
Buffering isn’t as important on the LAN (this is why you are normally pressured to buy ‘cut through’ devices)
  Change the math to make the Latency 1ms and the expectation 10Gbps = 1.25MB
  ‘Cut through’ and low latency switches are designed for the data center, and can handle typical data center loads that don’t require buffering (e.g. same to same speeds, destinations within the broadcast domain)
Buffering *MATTERS* for WAN Transfers
  Placing something with inadequate buffering in the path reduces the buffer for the entire path. E.g. if you have an expectation of 10Gbps over 100ms – don’t place a 12MB buffer anywhere in there – your reality is now ~10x less than it was before (e.g. 10Gbps @ 10ms, or 1Gbps @ 100ms)

## Slide 30: TCP’s Congestion Control
50ms simulated RTT
Congestion w/ 2Gbps UDP traffic
HTCP / Linux 2.6.32
Slide from Michael Smitasin, LBLnet

## Slide 31: Outline
Introduction
Solution Space
  Understanding the Solution Space (Users, Use Cases, Long Term Impacts)
  Preliminaries (e.g. Network Protocols 101)
  Architecture & Design
  Monitoring and Measurement
  Data Mobility
  Security and Policy
Putting it Together
Conclusions / QA

## Slide 32: Test and Measurement – Keeping the Network Clean
The wide area network, the Science DMZ, and all its systems can be functioning perfectly
Eventually something is going to break
  Networks and systems are built with many, many components
  Sometimes things just break – this is why we buy support contracts
Other problems arise as well – bugs, mistakes, whatever
We must be able to find and fix problems when they occur
Why is this so important? Because we use TCP!
Notes: Remember one of the pieces was perfSONAR?

## Slide 33: Soft Network Failures
Soft failures are where basic connectivity functions, but high performance is not possible.
TCP was intentionally designed to hide all transmission errors from the user:
  “As long as the TCPs continue to function properly and the internet system does not become completely partitioned, no transmission errors will affect the users.” (From IEN 129, RFC 716)
Some soft failures only affect high bandwidth long RTT flows.
Hard failures are easy to detect & fix
  soft failures can lie hidden for years!
One network problem can often mask others

## Slide 34: perfSONAR
Network diagrams throughout these materials have little perfSONAR boxes everywhere
  The reason for this is that consistent behavior requires correctness
  Correctness requires the ability to find and fix problems
    You can’t fix what you can’t find
    You can’t find what you can’t see
    perfSONAR lets you see
Especially important when deploying high performance services
  If there is a problem with the infrastructure, need to fix it
  If the problem is not with your stuff, need to prove it
    Many players in an end to end path
    Ability to show correct behavior aids in problem localization

## Slide 35: Outline
Introduction
Solution Space
  Understanding the Solution Space (Users, Use Cases, Long Term Impacts)
  Preliminaries (e.g. Network Protocols 101)
  Architecture & Design
  Monitoring and Measurement
  Data Mobility
  Security and Policy
Putting it Together
Conclusions / QA

## Slide 36: Solution Space – Data Mobility
DTN History & Purpose:
  Original concept came from initial Science DMZ Design (~2012)
  Basic idea:
    Host(s) dedicated to the task of data movement (and only data movement)
    Limited application set (data movement tools), and users (rarely shell access)
    Specific security policy enforced on the switch/router ACLs
      Ports for data movement tools, most in a ‘closed wait’ state
      Nothing to impact the data channel
    Typically 2 footed:
      Limited reach into local network (e.g. ‘control channel’: shared filesystem, instruments)
      WAN piece that the data tools use (e.g. ‘data channel’)
  Position this, and the pS node, in the DMZ enclave near the border

## Slide 37: Solution Space – Data Mobility
40G/100G
Downstream
10G
10G
10G
Notes: Next two classes are the same from a systems perspective
(main different from a workflow perspective—i.e. double copy workflow for SANs but not with distributed/global file systems)
We see these storage architectures in DTNs at data and HPC facilities
But whatever you choose for storage will depend on your environment, requirements, and resources.
______________________
System reasoning: what kind of card used on the backend to the storage system—FC/Ethernet/Inifiniband look the same
But the workflow is what’s different
No block device communication between DTN kernel Global fs
For SAN and internal disks—DTN kernel sees it as “owning”/managing blocks in SAN or RAID
_____________________________
Distributed file systems—high quality of service
much more reliable
easy to manage
however, typically performance is much lower because they are usually a shared system—don’t know the workload of other users—possibility of contesting traffic
i.e., we see this at data centers/supercomputers
they do have bottlenecks. I/O is the storage controller (EMC is limited to 8G right now)
Same I/O capacity but no bottleneck with infiniband connections.
enterprise level system
IB
56 G/link and easy to aggregate
reliable networking—no packet loss
fairly cheap
Distributed filesystem: this is similar to the storage system, except that the exported volumes are not RAW but file system (PNFS, Lustre, GPFS…). This set up is typical of a tiered system: data is acquired and processed, and stored. Then the DTN read from the shared storage.
Storage Systems: These are usually more massive systems (EMC, Netapp, DDN, etc) providing raw volumes to servers. The connectivity is usually fiber, but it can also be infiniband and ethernet.
This class benefits storage capacity.
POINT: look at what your infrastructure requirements are
how much capacity do you need for the next 3 years—will your system scale the way you want?
how reliable does your storage have to be—source of truth or is it a pain to resend the data if a disk goes down? (i.e., choose your RAID appropriately)
performance of storage what you need? If its 10G—laptops won’t do that
don’t need to invest in super fast storage if you only want to use laptops

## Slide 38: Solution Space – Data Mobility
40G/100G
Downstream
10G
10G
10G
Notes: Next two classes are the same from a systems perspective
(main different from a workflow perspective—i.e. double copy workflow for SANs but not with distributed/global file systems)
We see these storage architectures in DTNs at data and HPC facilities
But whatever you choose for storage will depend on your environment, requirements, and resources.
______________________
System reasoning: what kind of card used on the backend to the storage system—FC/Ethernet/Inifiniband look the same
But the workflow is what’s different
No block device communication between DTN kernel Global fs
For SAN and internal disks—DTN kernel sees it as “owning”/managing blocks in SAN or RAID
_____________________________
Distributed file systems—high quality of service
much more reliable
easy to manage
however, typically performance is much lower because they are usually a shared system—don’t know the workload of other users—possibility of contesting traffic
i.e., we see this at data centers/supercomputers
they do have bottlenecks. I/O is the storage controller (EMC is limited to 8G right now)
Same I/O capacity but no bottleneck with infiniband connections.
enterprise level system
IB
56 G/link and easy to aggregate
reliable networking—no packet loss
fairly cheap
Distributed filesystem: this is similar to the storage system, except that the exported volumes are not RAW but file system (PNFS, Lustre, GPFS…). This set up is typical of a tiered system: data is acquired and processed, and stored. Then the DTN read from the shared storage.
Storage Systems: These are usually more massive systems (EMC, Netapp, DDN, etc) providing raw volumes to servers. The connectivity is usually fiber, but it can also be infiniband and ethernet.
This class benefits storage capacity.
POINT: look at what your infrastructure requirements are
how much capacity do you need for the next 3 years—will your system scale the way you want?
how reliable does your storage have to be—source of truth or is it a pain to resend the data if a disk goes down? (i.e., choose your RAID appropriately)
performance of storage what you need? If its 10G—laptops won’t do that
don’t need to invest in super fast storage if you only want to use laptops

## Slide 39: Software – Data Transfer
Using the right data transfer tool is STILL very important
Sample Results: Berkeley, CA to Argonne, IL (near Chicago ) RTT = 53 ms, network capacity = 10Gbps.
Notes
  scp is 24x slower than GridFTP on this path!!
  to get more than 1 Gbps (125 MB/s) disk to disk requires RAID array.
  Assume host TCP buffers are set correctly for the RTT
Tool | Throughput
scp | 330 Mbps
wget, GridFTP, FDT, 1 stream | 6 Gbps
GridFTP and FDT, 4 streams | 8 Gbps (disk limited)

## Slide 40: Data Transfer Performance and Expectations
This table available at:
http://fasterdata.es.net/fasterdata-home/requirements-and-expectations/

## Slide 41: Data Transfer Scorecard with Rates by Audience
A benchmark table is provided to gauge data architecture performance, which can vary depending on number of files, folders, size of files, distance between sites, CI performance (network, server, disk/filesystem), as well as data transfer tool.
https://fasterdata.es.net/DTN/data-transfer-scorecard/
Host Transfer Rates | ⅙ PetaScale (Minimum) | ⅓ PetaScale | ½ PetaScale |  | PetaScale: 1 PB/wk | PetaScale: 1 PB/day
 | 10G Capable DTN |  |  |  | 10xG, 25G, 40G, 100G DTNs | 
Data Transfer Rate/Volume (Researcher) | 1 TB/hr | 2 TB/hr | 3 TB/hr |  | 5.95 TB/hr | 41.67 TB/hr
Network Transfer Rate (Network Admin) | 2.22 Gb/s | 4.44 Gb/s | 6.67 Gb/s |  | 13.23 Gb/s | 92.59 Gb/s
Storage Transfer Rate (Sys/Storage Admin) | 277.78 MB/s | 555.54 MB/s | 833.33 MB/s |  | 1.65 GB/s | 11.57 GB/s

## Slide 42: To Reiterate:
Data movement is hard to get right
Lots of moving parts
  Software, Servers, Networks, and People
Testing will reveal that it may not be ideal
Testing will also motivate you to make it ideal
Shared experience around the community – lift all the boats, share all the knowledge, etc.

## Slide 43: Outline
Introduction
Solution Space
  Understanding the Solution Space (Users, Use Cases, Long Term Impacts)
  Preliminaries (e.g. Network Protocols 101)
  Architecture & Design
  Monitoring and Measurement
  Data Mobility
  Security and Policy
Putting it Together
Conclusions / QA

## Slide 44: Science DMZ Security
Goal: Disentangle security policy and enforcement for science flows from enterprise / business systems
Rationale
  Science data traffic is simple from a security perspective
  Narrow application set on Science DMZ
    Data transfer, data streaming packages
    No printers, document readers, web browsers, building control systems, financial databases, staff desktops, etc.
  Security controls that are typically implemented to protect business resources routinely cause performance problems
Separation allows each to be optimized

## Slide 45: Science DMZ as Security Architecture
Allows for better segmentation of risks, more granular application of controls to those segmented risks.
  Limit risk profile for high-performance data transfer applications
  Apply specific controls to data transfer hosts
  Avoid including unnecessary risks, unnecessary controls
Remove degrees of freedom – focus only on what is necessary
  Easier to secure
  Easier to achieve performance
  Easier to troubleshoot

## Slide 46: Network Segmentation
Think about residence hall networks, business application networks, and the networks that are primarily in research areas:
  The risk profiles are clearly different
  It makes sense to segment along these lines
Your institution may already be doing this for things like HIPAA and PCI-DSS. Why? Because of the controls!
The Science DMZ follows the same concept, from a security perspective.
Using a Science DMZ to segment research traffic (especially traffic from specialized research instruments) can actually improve campus security posture.

## Slide 47: Outline
Introduction
Solution Space
Putting it Together
Conclusions / QA

## Slide 48: Collaboration Within The Organization
All stakeholders should collaborate on Science DMZ design, policy, and enforcement
The security people have to be on board
  Remember: security people already have political cover – it’s called the firewall
  If a host gets compromised, the security officer can say they did their due diligence because there was a firewall in place
  If the deployment of a Science DMZ is going to jeopardize the job of the security officer, expect pushback
The Science DMZ is a strategic asset, and should be understood by the strategic thinkers in the organization
  Changes in security models
  Changes in operational models
  Enhanced ability to compete for funding
  Increased institutional capability – greater science output

## Slide 49: Sensible Usage Policies
Everything we designed today was meant to be ‘used’ by the scientific community. What does that mean?
  Do you need to allow them to plug in their old windows laptop directly to the border router?
  Remember all that work you did to understand use cases? Let's revisit that instead:
Data mobility (in a nutshell):
  I need research data
    I can create it, or I can retrieve it
  Once I have it, I shall analyze it
    That could be local, it may not be
  After analysis I must do something with it
    Maybe I delete it? Who am I kidding … I want to hold it forever!

## Slide 50: Sensible Usage Policies
Define access methods
  E.g. shared DTN that plugs into storage vs. someone’s laptop
  Tools that can be used
  People who get accounts
  Consider: http://fasterdata.es.net/science-dmz/science-dmz-users/
Define AUP
  What can/should/will be sent across the infrastructure
  What happens when something bad occurs
  How often the AUP is reviewed
  Consider: http://fasterdata.es.net/science-dmz/usage-policy/
Define monitoring/measurement/security expectations
  Let the pros monitor/keep things up to date
  Let the users just use
BE TRANSPARENT

## Slide 51: Putting it All Together
Know the users, know the use cases
Data Architecture – e.g. support the ingress and egress of information at all layers
  Network Gear
  Data Transfer Software / Hardware
  Measurement / Monitoring
  Security Infrastructure
Facilitate Usage
Have a good story for long term usage/onboarding/expansion/maintenance

## Slide 52: Outline
Introduction
Solution Space
Putting it Together
Conclusions / QA

## Slide 53: Questions?
EPOC Helpdesk (send in anything you want):
  epoc@tacc.utexas.edu

## Slide 54
National Science Foundation Award #1826994
Designing, Building, & Maintaining
a Science DMZ and Data Architecture
Modern Cyberinfrastructure for Research Data Management Workshop
University of Central Florida
February 16-17, 2023
https://epoc.global
Ken Miller, Jason Zurawski
ken@es.net, zurawski@es.net
ESnet / Lawrence Berkeley National Laboratory