## Slide 1
National Science Foundation Award #1826994
perfSONAR Topics
Modern Cyberinfrastructure for Research Data Management Workshop
University of Central Florida
February 16-17, 2023
https://epoc.global
Ken Miller, Jason Zurawski
ken@es.net, zurawski@es.net
ESnet / Lawrence Berkeley National Laboratory

## Slide 2: Outline
Problem Statement on Network Connectivity
Supporting Scientific Users
Network Performance & TCP Behaviors w/ Packet Loss
What is perfSONAR
Deployment Overview
Command's & Syntax
Examples
Conclusions
Notes: Make the point that the complexity of the network is too much for anyone to grasp – and with the complexity we need tools/methods to bite off smaller parts of the problem

## Slide 3: Problem Statement
The global Research & Education network ecosystem is comprised of hundreds of international, national, regional and local-scale networks.
Notes: Make the point that the complexity of the network is too much for anyone to grasp – and with the complexity we need tools/methods to bite off smaller parts of the problem

## Slide 4: Problem Statement
While these networks all interconnect, each network is owned and operated by separate organizations (called “domains”) with different policies, customers, funding models, hardware, bandwidth and configurations.
Notes: MAP is courtesy of the GLIF
perfSONAR is designed to be multi-domain, so drive home the fact that all transfers are multi-domain

## Slide 5: The R&E Community
The global Research & Education network ecosystem is comprised of hundreds of international, national, regional and local-scale resources – each independently owned and operated.
This complex, heterogeneous set of networks must operate seamlessly from “end to end” to support science and research collaborations that are distributed globally.
Data mobility is required; there is no liquid market for HPC resources (people use what they can get – DOE, XSEDE, NOAA, etc. etc.)
  To stay competitive, we must learn the use patterns, and support them
  This may mean making sure your network, and the networks of others, are functional
Notes: Getting into the end to end argument – we can’t just ensure things work locally.

## Slide 6: Outline
Problem Statement on Network Connectivity
Supporting Scientific Users
Network Performance & TCP Behaviors w/ Packet Loss
What is perfSONAR
Deployment Overview
Command's & Syntax
Examples
Conclusions
Notes: Make the point that the complexity of the network is too much for anyone to grasp – and with the complexity we need tools/methods to bite off smaller parts of the problem

## Slide 7: Understanding Data Trends
http://www.es.net/science-engagement/science-requirements-reviews/
Notes: This comes from ESnet requirements review data (starting in 2007). Smaller collaborations produce less data than larger ones, but their numbers are greater. Across the board increases as instrumentation, processing, storage, becomes better/more widely available.

## Slide 8: Challenges to Network Adoption
Causes of performance issues are complicated for users.
Lack of communication and collaboration between the CIO’s office and researchers on campus.
Lack of IT expertise within a science collaboration or experimental facility
User’s performance expectations are low (“The network is too slow”, “I tried it and it didn’t work”).
Cultural change is hard (“we’ve always shipped disks!”).
Scientists want to do science not IT support
The Capability Gap
Notes: Reasons why it is hard for users to embrace networks – its challenging to get things working.

## Slide 9: Outline
Problem Statement on Network Connectivity
Supporting Scientific Users
Network Performance & TCP Behaviors w/ Packet Loss
What is perfSONAR
Deployment Overview
Command's & Syntax
Examples
Conclusions
Notes: Make the point that the complexity of the network is too much for anyone to grasp – and with the complexity we need tools/methods to bite off smaller parts of the problem

## Slide 10: Let’s Talk Performance …
"In any large system, there is always something broken.”
- Jon Postel
Modern networks are occasionally designed to be one-size-fits-most
  e.g. if you have ever heard the phrase “converged network”, the design is to facilitate CIA (Confidentiality, Integrity, Availability)
It’s all TCP
  Bulk data movement is a common thread (move the data from the microscope, to the storage,
to the processing, to the people – and they are all sitting in different facilities)
  This fails when TCP suffers due to path problems (ANYWHERE in the path)
  It’s easier to work with TCP than to fix it (20+ years of trying…)
TCP suffers the most from unpredictability; Packet loss/delays are the enemy
  Small buffers on the network gear and hosts
  Incorrect application choice
  Packet disruption caused by overzealous security
  Congestion from herds of mice
It all starts with knowing your users, and knowing your network
Notes: Why is it a challenge? It’s the complexity, and it’s the tools.
We basically need to accommodate TCP to do anything useful.

## Slide 11: Where Are The Problems?
Source
Campus
Backbone
S
NREN
Congested or faulty links between domains
Congested intra- campus links
D
Destination
Campus
Latency dependant problems inside domains with small RTT
Regional
Notes: Isolating problems is challenging – consider the following sets of domains. If things are ‘slow’, it could be anything (or multiple things)
We need something that examines the entire path, and pulls out trouble

## Slide 12: Local Testing Will Not Find Everything
Source
Campus
R&E
Backbone
Regional
D
S
Destination
Campus
Regional
Performance is good when RTT is < ~10 ms
Performance is poor when RTT exceeds ~10 ms
Switch with small buffers
Notes: The magic buffer zone – if we are < 10ms, we often don’t see problems. Throughput still works well because TCP can perform well over short distances with lots of loss.
As we get further out, we notice the pain.
This leads to some false diagnostics at times – e.g. if we have a problem locally, but we only see it when we go far away, its tempting to say the problem is out there, far away. See the switch with small buffers locally as the example.

## Slide 13: Soft Failures Cause Packet Loss and Degraded TCP Performance
Metro Area
Local
(LAN)
Regional
Continental
International
Measured (TCP Reno)
Measured (HTCP)
Theoretical (TCP Reno)
Measured (no loss)
With loss, high performance beyond metro distances is essentially impossible
Notes: TCP works well over short distances (e.g. 1% packet loss on the LAN will produce high throughput).
The further out you get the more pronounced the problems will be as the algorithms cope with retransmissions.

## Slide 14: Soft Network Failures
Soft failures are where basic connectivity functions, but high performance is not possible.
TCP was intentionally designed to hide all transmission errors from the user:
  “As long as the TCPs continue to function properly and the internet system does not become completely partitioned, no transmission errors will affect the users.” (From IEN 129, RFC 716)
Some soft failures only affect high bandwidth long RTT flows.
Hard failures are easy to detect & fix
  soft failures can lie hidden for years!
One network problem can often mask others
Notes: Introduce the soft network failure – not a loss of connectivity. This is what perfSONAR is designed to find since they are challenging to see unless you are testing end to end over a large distance.

## Slide 15: Problem Statement: Hard vs. Soft Failures
“Hard failures” are the kind of problems every organization understands
  Fiber cut
  Power failure takes down routers
  Hardware ceases to function
Classic monitoring systems are good at alerting hard failures
  i.e., NOC sees something turn red on their screen
  Engineers paged by monitoring systems
“Soft failures” are different and often go undetected
  Basic connectivity (ping, traceroute, web pages, email) works
  Performance is just poor
How much should we care about soft failures?
Notes: Answer: we need to care *a lot* about soft failures – see next

## Slide 16: Causes of Packet Loss
Network Congestion
  Easy to confirm via SNMP, easy to fix with $$
  This is not a ‘soft failure’, but just a network capacity issue
  Often people assume congestion is the issue when it fact it is not.
Under-buffered switch dropping packets
  Hard to confirm
Under-powered firewall dropping packets
  Hard to confirm
Dirty fibers or connectors, failing optics/light levels
  Sometimes easy to confirm by looking at error counters in the routers
Overloaded or slow receive host dropping packets
  Easy to confirm by looking at CPU load on the host

## Slide 17: Under-buffered Switches are probably our biggest problem today
Notes: Testing done by Michael Smitasin , LBL
1 10G TCP flow competing with 2GB background UDP

## Slide 18: Outline
Problem Statement on Network Connectivity
Supporting Scientific Users
Network Performance & TCP Behaviors w/ Packet Loss
What is perfSONAR
Deployment Overview
Command's & Syntax
Examples
Conclusions
Notes: Make the point that the complexity of the network is too much for anyone to grasp – and with the complexity we need tools/methods to bite off smaller parts of the problem

## Slide 19: But … It’s Not Just the Network
Perhaps you are saying to yourself “I have no control over parts of my campus, let alone the 5 networks that sit between me and my collaborators”
  Significant gains are possible in isolated areas of the OSI Stack
Things “you” control:
  Choice of data movement applications (say no to SCP and RSYNC)
  Configuration of local gear (hosts, network devices)
  Placement and configuration of diagnostic tools, e.g. perfSONAR
  Use of the diagnostic tools
Things that need some help:
  Configuration of remote gear
  Addressing issues when the diagnostic tools alarm
  Getting someone to “care”
Notes: Don’t stop at network architecture, fix other stuff too

## Slide 20: Network Monitoring
All networks do some form monitoring.
  Addresses needs of local staff for understanding state of the network
    Would this information be useful to external users?
    Can these tools function on a multi-domain basis?
Beyond passive methods, there are active tools.
  E.g. often we want a ‘throughput’ number. Can we automate that idea?
  Wouldn’t it be nice to get some sort of plot of performance over the course of a day? Week? Year? Multiple endpoints?
perfSONAR = Measurement Middleware
Notes: Everyone does it – but not everyone monitors end to end
perfSONAR is nothing earth shattering, it’s a way to share measurements and make it easy to deploy/figure out what is going on

## Slide 21: perfSONAR
All the previous Science DMZ network diagrams have little perfSONAR boxes everywhere
  The reason for this is that consistent behavior requires correctness
  Correctness requires the ability to find and fix problems
    You can’t fix what you can’t find
    You can’t find what you can’t see
    perfSONAR lets you see
Especially important when deploying high performance services
  If there is a problem with the infrastructure, need to fix it
  If the problem is not with your stuff, need to prove it
    Many players in an end to end path
    Ability to show correct behavior aids in problem localization
Notes: perfSONAR = visbibility

## Slide 22: What is perfSONAR?
perfSONAR is a tool coordinated suite of tools to:
  Set network performance expectations
  Find network problems (“soft failures”)
  Helps coordinate fixing these problems
… all in multi-domain environments
These problems are all harder when multiple networks are involved
perfSONAR provides a standardized way to publish active and passive monitoring data
  This data is interesting to network researchers as well as network operators
Notes: Enables Federation
  Service oriented
  Designed with ‘multi-domain’ in mind
Brings together useful tools to address different needs
  Several active and passive tools
  Interface to configure regular testing
  Diagnostic tools ready with ‘0 configuration’
Easy to install, easy to use
  ISO image can be burned to CD/USB key
  ‘Wizard’ interface for configuration
Encouraging people to deploy ‘known good’ measurement points near domain boundaries
  “known good” = hosts that are well configured, enough memory and CPU to drive the network, proper TCP tuning, clean path, etc.
Community Adoption
  Over 1300 instances seen world wide
  40+ countries
  100s of domains

## Slide 23: perfSONAR History
perfSONAR can trace its origin to the Internet2 “End 2 End performance Initiative” from the year 2000. What has changed since then?
  The Good News:
    TCP is much less fragile; Cubic is the default CC alg, autotuning is and larger TCP buffers are everywhere
    Reliable parallel transfers via tools like Globus Online
    High-performance UDP-based commercial tools like Aspera
  The Bad News:
    The wizard gap is still large
    Jumbo frame use is still small
    Under-buffered and switches and routers are still common
    Under-powered/misconfigured firewalls are common
    Soft failures still go undetected for months
    Users still might not know or understand what kind of performance to expect
Notes: Improvements in 15 years since the idea came about – but lots of room to grow

## Slide 24: Simulating Performance
It’s infeasible to perform at-scale data movement all the time – as we see in other forms of science, we need to rely on simulations
Network performance comes down to a couple of key metrics:
  Throughput (e.g. “how much can I get out of the network”)
  Latency (time it takes to get to/from a destination)
  Packet loss/duplication/ordering (for some sampling of packets, do they all make it to the other side without serious abnormalities occurring?)
  Network utilization (the opposite of “throughput” for a moment in time)
We can get many of these from a selection of active and passive measurement tools – enter the perfSONAR Toolkit
Notes: Idea – we are measuring performance by testing what is possible. If OWAMP runs stable and loss free, video will work out ok. If throughput is stable and high, bulk data movement should work on the network (does not test disk)

## Slide 25: perfSONAR Toolkit
The “perfSONAR Toolkit” is an open source implementation and packaging of the perfSONAR measurement infrastructure and protocols
  http://docs.perfsonar.net/install_getting.html
All components are available as RPMs, DEBs, and bundled as CentOS 7, Debian 9 or Ubuntu 16 and 18-based packages (as of perfSONAR v. 4.2.4)
  perfSONAR tools are much more accurate if run on a dedicated perfSONAR host
Very easy to install and configure
  Usually takes less than 30 minutes
Notes: Install via the ISO – RPMs if you don’t want to do that

## Slide 26: Outline
Problem Statement on Network Connectivity
Supporting Scientific Users
Network Performance & TCP Behaviors w/ Packet Loss
What is perfSONAR
Deployment Overview
Command's & Syntax
Examples
Conclusions
Notes: Make the point that the complexity of the network is too much for anyone to grasp – and with the complexity we need tools/methods to bite off smaller parts of the problem

## Slide 27: Toolkit “Beacon” Use Case
The general use case is to establish some set of tests to other locations/facilities
To answer the what/why questions:
  Regular testing with select tools helps to establish patterns – how much bandwidth we would see during the course of the day – or when packet loss appears
  We do this to ‘points of interest’ to see how well a real activity (e.g. Globus transfer) would do.
If performance is ‘bad’, don’t expect much from the data movement tool
Notes: General use case – make the tools available and let people test against you

## Slide 28: Benefits: Finding needles in haystacks
Above all, perfSONAR allows you to maintain a healthy, high-performing network because it helps identify the “soft failures” in the network path.
  Classical monitoring systems have limitations
    Performance problems are often only visible at the ends
    Individual network components (e.g. routers) have no knowledge of end host state
  perfSONAR tests the network in ways that classical monitoring systems do not
More perfSONAR distributions equal better network visibility.
Notes: Metcalf law argument – only useful because people are using it

## Slide 29: http://stats.es.net/ServicesDirectory/
Notes: View public instances

## Slide 30: perfSONAR Dashboard: Raising Expectations and improving network visibility
Status at-a-glance
Packet loss
Throughput
Correctness
Current live instances at http://pas.net.internet2.edu/
http://ps-dashboard.es.net/
Drill-down capabilities:
Test history between hosts
Ability to correlate with other events
Very valuable for fault localization and isolation
Notes: Dashboards – requires coordination of testing

## Slide 31: Outline
Problem Statement on Network Connectivity
Supporting Scientific Users
Network Performance & TCP Behaviors w/ Packet Loss
What is perfSONAR
Deployment Overview
Command's & Syntax
Examples
Conclusions
Notes: Make the point that the complexity of the network is too much for anyone to grasp – and with the complexity we need tools/methods to bite off smaller parts of the problem

## Slide 32: pscheduler – The Secret Sauce
pscheduler is the engine that drives perfSONAR
  Coordinates timeslots and schedules tests between nodes
  Creates a common syntax that all tools use
  Handles the storage of results
This approach to test management ensures that:
  Tests that could impact each other’s performance, like throughput, are never run simultaneously
  Simplified coordination, where you don’t need an engineer at the other end to start a daemon, open a port, etc.
  Access control is maintained and test limits are enforced

## Slide 33: Basic syntax
pscheduler task [options] test-type [test-options]
  task is what you want pscheduler to do
  test-type is how you want pscheduler to do it
There’s more than one tool to run many of these tests, and pscheduler gives you the option to choose that tool:
  iperf2/iperf3/nuttcp for bandwidth
  traceroute/tracepath/paris-traceroute for routing
  --help is your friend!

## Slide 34: Remote Commands, AKA, Your Best Friends
--source and --dest flags do what you expect they would, but neither end has to be your node
  You can run most tests between two remote nodes
  This includes perfSONAR’s built-in self-diagnostic tools
This core piece of functionality is what makes perfSONAR useful in day-to-day troubleshooting activities and makes it more than just a simple performance data collector

## Slide 37: Outline
Problem Statement on Network Connectivity
Supporting Scientific Users
Network Performance & TCP Behaviors w/ Packet Loss
What is perfSONAR
Deployment Overview
Command's & Syntax
Examples
Conclusions
Notes: Make the point that the complexity of the network is too much for anyone to grasp – and with the complexity we need tools/methods to bite off smaller parts of the problem

## Slide 38: NRAO/UVA <> SARAO Performance Problem
Data sharing from the National Radio Astronomy Observatory, located on the University of Virginia campus, to the South African Radio Astronomy Observatory
  Low performance – 4.8Mbps
Initial testing from the South African side revealed a few potential problems, such as asymmetric routing and paths with unnecessarily circuitous routes.
  These were identified using normal traceroutes and quickly corrected
  No appreciable change in performance

## Slide 39: Identification of possible pS toolkits
1 te0-1-0-1-cpt2-pe1.net.tenet.ac.za (155.232.40.9) AS2018 0.703 ms
…
5 155.232.71.3 AS2018 166.6 ms
TENET-1, ZA
6 et-3-3-0.4079.rtsw.atla.net.internet2.edu (162.252.70.42) AS11537 172.712 ms
INTERNET2-RESEARCH-EDU, US
7 ae-4.4079.rtsw.wash.net.internet2.edu (198.71.45.7) AS11537 185.775 ms
INTERNET2-RESEARCH-EDU, US
8 ae-0.4079.rtsw2.ashb.net.internet2.edu (162.252.70.137) AS11537 186.419 ms
INTERNET2-RESEARCH-EDU, US
9 ae-2.4079.rtsw.ashb.net.internet2.edu (162.252.70.74) AS11537 185.845 ms
INTERNET2-RESEARCH-EDU, US
10 192.122.175.14 AS40220 186.368 ms
MARIA, US
11 br01-udc-et-1-0-0-20.net.virginia.edu (192.35.48.33) AS225 188.065 ms
VIRGINIA-AS, US
12 cr01-udc-et-4-2-0.net.virginia.edu (128.143.236.6) AS225 188.448 ms
VIRGINIA-AS, US
13 cr01-gil-et-7-0-0.net.virginia.edu (128.143.236.89) AS225 203.281 ms
VIRGINIA-AS, US
14 perfsonar-10.cv.nrao.edu (198.51.208.55) AS225 188.179 ms
VIRGINIA-AS, US

## Slide 40: perfSONAR Lookup Service Directory
http://stats.es.net/ServicesDirectory/
Lookup listed testpoints and toolkits by almost any criteria:
Hostname
IP address
Institution
City
Country
REN
pS instance must have commodity internet access to be listed.

## Slide 41: Initial problem isolation
Tests from various domestic and international perfSONAR nodes to UVAs campus were telling:
  CHPC South Africa -> Internet2 Washington - 6.67 Gbps
  Internet2 Albany -> Internet2 Washington - 9.893 Gbps
  Internet2 Washington -> NRAO - 3.31 Gbps (lots of retries)
  Internet2 Washington -> HPC University Virginia - 2.21 Gbps (lots of retries)
  NRAO -> HPC University Virginia - 6.64 Gbps (lots of retries)

## Slide 42: UVA/NRAO Network
MTU 9000
MTU 1500?

## Slide 43: Path MTU Discovery (PMTUD)
Is a layer 3 construct
Requires UDP and ICMP to function
  UDP packets larger than the MTU setting of the receiving router interface will trigger an ICMP “unreachable” message back to the sending router, which in turn causes a renegotiation to a lower MTU
All is not lost if PMTUD doesn’t work
  Smart transfer tools can figure out a common MTU, at the cost of time
  Packets sent at 9K can be fragmented to adhere to a smaller MTU, at the cost of performance…unless the no-fragment flag is set
  Neither of these scenarios is good for high performance. PMTUD should be made to work and common MTUs enforced wherever possible

## Slide 44: Further isolation
Working inward from a known good ESnet perfSONAR node to UVA:
Interval Throughput Retransmits Current Window
0.0 - 1.0 9.13 Gbps 22 33.17 MBytes
1.0 - 2.0 9.35 Gbps 0 33.58 MBytes
2.0 - 3.0 9.38 Gbps 0 33.58 MBytes
3.0 - 4.0 9.38 Gbps 0 33.58 MBytes
4.0 - 5.0 9.38 Gbps 0 33.58 MBytes
5.0 - 6.0 9.35 Gbps 0 33.58 MBytes
6.0 - 7.0 9.36 Gbps 0 33.58 MBytes
7.0 - 8.0 9.38 Gbps 0 33.58 MBytes
8.0 - 9.0 9.37 Gbps 0 33.58 MBytes
9.0 - 10.0 9.37 Gbps 0 33.58 MBytes
Summary
Interval Throughput Retransmits Receiver Throughput
0.0 - 10.0 9.35 Gbps 22 9.25 Gbps
This test looks good, because the hosts successfully negotiate 1500 MTU

## Slide 45: Negotiations break down
Working inward from a known good ESnet perfSONAR node to NRAO:
(Keep in mind, we know MTU 9000 on both ends, but with a step down to 1500 in the middle of the UVA campus)
Interval Throughput Retransmits Current Window
0.0 - 1.0 2.54 Mbps 2 8.95 KBytes
1.0 - 2.0 0.00bps 1 8.95 KBytes
2.0 - 3.0 0.00bps 0 8.95 KBytes
3.0 - 4.0 0.00bps 31 3.07 KBytes
4.0 - 5.0 0.00bps 67 5.12 KBytes
5.0 - 6.0 4.45 Mbps 2 17.41 KBytes
6.0 - 7.0 8.26 Mbps 0 33.79 KBytes
7.0 - 8.0 23.28 Mbps 0 94.21 KBytes
8.0 - 9.0 51.75 Mbps 0 218.11 KBytes
9.0 - 10.0 83.88 Mbps 0 392.19 KBytes
Summary
Interval Throughput Retransmits Receiver Throughput
0.0 - 10.0 17.42 Mbps 103 10.29 Mbps
9000B packets failing
1500B packets after re-negotiation

## Slide 46: Traceroute: ESnet to NRAO
traceroute to perfsonar-10.cv.nrao.edu (198.51.208.55), 30 hops max, 60 byte packets
1 esneteastrt1-eastdcpt1.es.net (198.124.238.37) 0.549 ms 0.544 ms 0.547 ms
2 newycr5-ip-a-esneteastrt1.es.net (198.124.218.17) 1.969 ms 1.963 ms 1.953 ms
3 aofacr5-ip-a-newycr5.es.net (134.55.37.77) 2.330 ms 2.304 ms 2.313 ms
4 et-2-1-5.197.rtsw.newy32aoa.net.internet2.edu (64.57.28.14) 2.323 ms 2.324 ms 2.327 ms
5 ae-3.4079.rtsw.wash.net.internet2.edu (162.252.70.138) 7.571 ms 7.672 ms 7.528 ms
6 ae-0.4079.rtsw2.ashb.net.internet2.edu (162.252.70.137) 8.095 ms 8.077 ms 8.061 ms
7 ae-2.4079.rtsw.ashb.net.internet2.edu (162.252.70.74) 28.089 ms 18.414 ms 18.454 ms
8 192.122.175.14 (192.122.175.14) 8.221 ms 8.179 ms 8.205 ms
9 br01-udc-et-1-0-0-20.net.virginia.edu (192.35.48.33) 10.310 ms 10.310 ms 10.383 ms
10 cr01-udc-et-4-2-0.net.virginia.edu (128.143.236.6) 12.609 ms 12.603 ms 12.638 ms
11 cr01-gil-et-7-0-0.net.virginia.edu (128.143.236.89) 12.407 ms 12.403 ms 12.393 ms
12 perfsonar-10.cv.nrao.edu (198.51.208.55) 10.058 ms 10.032 ms 10.022 ms
Well, that looks good. Let’s try tracepath and see where the MTU changes

## Slide 47: Tracepath: ESnet to NRAO
1?: [LOCALHOST] pmtu 9000
1: esneteastrt1-eastdcpt1.es.net 0.788ms
1: bnlmr2-bnlpt1.es.net 0.728ms
2: no reply
3: aofacr5-ip-b-newycr5.es.net 2.411ms asymm 2
4: et-2-1-5.197.rtsw.newy32aoa.net.internet2.edu 2.468ms asymm 3
5: ae-3.4079.rtsw.wash.net.internet2.edu 8.176ms asymm 4
6: ae-0.4079.rtsw2.ashb.net.internet2.edu 8.889ms asymm 5
7: ae-2.4079.rtsw.ashb.net.internet2.edu 8.242ms asymm 6
8: 192.122.175.14 8.522ms asymm 7
9: no reply
10: no reply
11: no reply
12: no reply
Traceroute works, but tracepath doesn’t??

## Slide 48: Different Tools, Different Packets
Traceroute uses small 60B UDP packets
Tracepath uses larger 64KB UDP packets
So, somewhere we have a roadblock. Small packets can make it through, but larger ones are dropped (not fragmented).
How do we figure out the max size? Trial and error. Start at 9K and cut the size in half until you get a response, then sneak back up until the packets disappear again.

## Slide 49: Tracepath: ESnet to NRAO, 1509 bytes
1: esneteastrt1-eastdcpt1.es.net 0.340ms
2: no reply
3: aofacr5-ip-a-newycr5.es.net 2.279ms asymm 2
4: et-2-1-5.197.rtsw.newy32aoa.net.internet2.edu 2.310ms asymm 3
5: ae-3.4079.rtsw.wash.net.internet2.edu 7.574ms asymm 4
6: ae-0.4079.rtsw2.ashb.net.internet2.edu 9.422ms asymm 5
7: ae-2.4079.rtsw.ashb.net.internet2.edu 7.986ms asymm 6
8: 192.122.175.14 8.123ms asymm 7
9: no reply
MARIA
UVA

## Slide 50: Tracepath: ESnet to NRAO, 1508 bytes
1: bnlmr2-bnlpt1.es.net 0.327ms
2: no reply
3: aofacr5-ip-b-newycr5.es.net 2.332ms asymm 2
4: et-2-1-5.197.rtsw.newy32aoa.net.internet2.edu 2.338ms asymm 3
5: ae-3.4079.rtsw.wash.net.internet2.edu 7.668ms asymm 4
6: ae-0.4079.rtsw2.ashb.net.internet2.edu 9.833ms asymm 5
7: ae-2.4079.rtsw.ashb.net.internet2.edu 7.872ms asymm 6
8: 192.122.175.14 8.166ms asymm 7
9: br01-udc-et-1-0-0-20.net.virginia.edu 9.998ms asymm 7
9?: br01-udc-et-1-0-0-20.net.virginia.edu asymm 7
10: cr01-udc-et-4-2-0.net.virginia.edu 10.470ms asymm 8
11: cr01-gil-et-7-0-0.net.virginia.edu 10.208ms asymm 9
12: cr01-gil-et-7-0-0.net.virginia.edu 10.253ms pmtu 1500
12: perfsonar-10.cv.nrao.edu 10.154ms !H
Resume: pmtu 1500
MARIA
UVA

## Slide 51: Problem located
The issue was between the MARIA router and the UVA router
  The MARIA interface was configured for MTU 9192
  The UVA interface was configured for MTU 1518
With PMTUD broken there was no hope for external MTU 9000 equipment to negotiate an appropriate MTU with the NRAO node
UVA changed the MTU on their router interface to match that of MARIA, while keeping their downstream equipment at their campus standard MTU 1500

## Slide 52: Yeah, yeah, but what about performance??
Before:
pscheduler task throughput --source cpt-chpc-10g.perfsonar.ac.za --dest perfsonar-10.cv.nrao.edu
Summary
Interval Throughput Retransmits Receiver Throughput
0.0 - 10.0 380.37 Kbps 58 108.18 Kbps
After:
pscheduler task throughput -t 30 --source cpt-chpc-10g.perfsonar.ac.za --dest perfsonar-10.cv.nrao.edu
Summary
Interval Throughput Retransmits Receiver Throughput
0.0 - 30.0 2.67 Gbps 0 2.62 Gbps

## Slide 53: Outline
Problem Statement on Network Connectivity
Supporting Scientific Users
Network Performance & TCP Behaviors w/ Packet Loss
What is perfSONAR
Deployment Overview
Conclusions
Notes: Make the point that the complexity of the network is too much for anyone to grasp – and with the complexity we need tools/methods to bite off smaller parts of the problem

## Slide 54: Benefit: Active and Growing Community
Active email lists and forums provide:
  Instant access to advice and expertise from the community.
  Ability to share metrics, experience and findings with others to help debug issues on a global scale.
Joining the community automatically increases the reach and power of perfSONAR
  The more endpoints means exponentially more ways to test and discover issues, compare metrics

## Slide 55: perfSONAR Community
The perfSONAR collaboration is working to build a strong user community to support the use and development of the software.
perfSONAR Mailing Lists
  Announcement Lists:
    https://lists.internet2.edu/sympa/subscribe/perfsonar-announce
  Users List:
    https://lists.internet2.edu/sympa/subscribe/perfsonar-user

## Slide 56: Resources
perfSONAR website
  http://www.perfsonar.net/
perfSONAR Documentation
  http://docs.perfsonar.net/
perfSONAR mailing lists
  http://www.perfsonar.net/about/getting-help/
perfSONAR directory
  http://stats.es.net/ServicesDirectory/
perfSONAR YouTube Channel
  https://www.youtube.com/channel/UCjK-P49pAKK9hUrrNbbe0Sg
FasterData Knowledgebase
  http://fasterdata.es.net/

## Slide 57
National Science Foundation Award #1826994
perfSONAR Topics
Modern Cyberinfrastructure for Research Data Management Workshop
University of Central Florida
February 16-17, 2023
https://epoc.global
Ken Miller, Jason Zurawski
ken@es.net, zurawski@es.net
ESnet / Lawrence Berkeley National Laboratory