## Slide 1
Stitching Together Innovation with FABRIC Users
Bluefield Data Processing Units (DPUs)
Elie Kfoury
Tuesday, November 11, 2025

## Slide 2
Welcome and Introduction

## Slide 3
Elie Kfoury
University of South Carolina | Assistant Professor

## Slide 4
Agenda
Need for hardware acceleration
Background on Data Processing Units (DPUs)
Bluefield-3 DPU
DOCA programming and demo
    P4 programming and demo
    Training material
    Q&A

## Slide 5
Growth of CPU Performance
End of Moore’s Law and Dennard Scaling, and the limit of Amdahl’s Law
Notes: This chart shows how the rate at which processor performance doubled has slowed over time. Up to the early 2000s, performance roughly doubled every 18–24 months in line with Moore’s Law and Dennard scaling. After around 2005, that doubling slowed dramatically as power and parallelism limits were reached, ending the era of rapid performance scaling

## Slide 6
Growth of CPU Performance
Link speeds continue to rise exponentially while CPU performance has plateaued

## Slide 7
Growth of CPU Performance
Link speeds continue to rise exponentially while CPU performance has plateaued
The gap between CPU performance and network speeds has led to domain-specific accelerators (DSAs)

## Slide 8
Data Processing Units (DPUs)
DPUs use DSAs to offload processing from general purpose CPU
  Programmable packet processing pipeline, regular expression, encryption/decryption, etc.
The DSAs are typically implemented on ASIC or FPGAs
DPUs also include general-purpose CPU cores for managing the system

## Slide 9
Data Processing Units (DPUs)
DPUs have been used to offload a variety of applications and infrastructure functions
Kfoury, Elie, et al. "A comprehensive survey on SmartNICs: Architectures, development models, applications, and research directions." IEEE Access (2024).

## Slide 10
DPUs Available Today
NVIDIA – BlueField family of Data Processing Units
AMD – Pensando and Alveo FPGA
Intel – Infrastructure Processing Units (IPUs)
Intel – FPGA variants (Silicom)
Marvell Octeon (DPU with ARM based CPU)
Others

## Slide 11
DPUs on FABRIC
BlueField-3 DPUs are being installed on various FABRIC sites
Currently the following sites have DPUs installed (more will be available soon): MASS, DALL, SALT, FIU, LOSA, NEWY, ATLA, HAWI

## Slide 12
BlueField-3 Architecture
BlueField-3 include programmable pipeline, datapath accelerator, ARM cores, and various DSAs

## Slide 13
DOCA Software Stack
DOCA is a comprehensive SDK, compilers, services, and tools for BlueField DPUs

## Slide 14
BlueField-3 Components
BlueField-3 include programmable pipeline, datapath accelerator, ARM cores, and DSAs
DOCA, DPDK, P4-DPDK

## Slide 15
BlueField-3 Components
BlueField-3 include programmable pipeline, datapath accelerator, ARM cores, and DSAs
C (RISC-V)

## Slide 16
BlueField-3 Components
BlueField-3 include programmable pipeline, datapath accelerator, ARM cores, and DSAs
P4, OvS HW offload, DOCA Flow

## Slide 17
DOCA Programming: Accelerator Invocation

## Slide 18
DOCA Programming
DOCA exposes APIs to invoke the accelerators (e.g., decompression, direct memory access (DMA), crypto, etc.)
The workflow consists of:
  Device discovery
  Create memory map (MMAP)
  Create & start a buffer inventory
  Create a Progress Engine (PE)
  Create and configure the accelerator instance
  Allocate and submit a task
  Drive progress & handle completion
  Cleanup

## Slide 19
Device Discovery
To work with DOCA libraries, an application must open a device available on the DPU
Open Device by PCI address

## Slide 20
Device Discovery
To work with DOCA libraries, an application must open a device available on the DPU
Open Device by PCI address
Open Device by capability

## Slide 21
Memory Map (Mmap)
doca_mmap serves as the memory pool for data buffers
The application provides a single memory region, as well as permissions for certain devices to access

## Slide 22
Buffer Inventory
doca_buf is the data buffer descriptor
This is not the actual data buffer, rather, it is a descriptor that holds metadata on the "pointed" data buffer
doca_buf_inventory serves as a pool of doca_buf

## Slide 23
Progress Engine (PE)
The progress engine PE is responsible for scheduling workloads (i.e., picking the next workload to execute).
PE enables asynchronous processing and handling of multiple tasks and events

## Slide 24
Accelerator Instance
Create an instance of the accelerator
  DOCA compress
  DOCA SHA
  DOCA RDMA
  DOCA DMA
  DOCA Ethernet
  DOCA Comch
  DOCA App Shield
  …

## Slide 25
Task Submission and Completion
Submit task and wait for completion

## Slide 26
Cleanup
Gracefully release everything to avoid leaks and dangling mappings
Make sure all tasks are complete before stopping/destroying resources

## Slide 27
DOCA Example on Artifact Manager
Compression acceleration example is available on the Artifact Manager

## Slide 28
Programming the Accelerated Pipeline with P4

## Slide 29
P4 Language
P4 emerged as domain-specific language to define packet processing:
  Define and parse new protocols
  Customize packet processing functions
  Offload packet processing from CPU

## Slide 30
PISA: Protocol Independent Switch Architecture
N. McKeown. Creating an End-to-End Programming Model for Packet Forwarding. Available: https://www.youtube.com/watch?v=fiBuao6YZl0&t=4216s

## Slide 31
DPL Overview
DOCA Pipeline Language (DPL) introduces a software development solution based on the P4 language
DPL is derived from the P4-16 language specification

## Slide 32
DPL Overview
DOCA Pipeline Language (DPL) introduces a software development solution based on the P4 language
DPL is derived from the P4-16 language specification

## Slide 33
P4 DPL Example
Simple L2 forwarding example available on Artifact Manager

## Slide 34
P4 DPL Example
Simple L2 forwarding example available on Artifact Manager

## Slide 35
P4 DPL Example
Simple L2 forwarding example available on Artifact Manager

## Slide 36
P4 Example on Artifact Manager
Simple L2 forwarding example available on Artifact Manager

## Slide 37
DPU Training Labs
on USC’s NETLAB

## Slide 38
DPU Labs
DPU cybertraining is supported by NSF Cybertraining program, award #2417823
Lab libraries available to learn about DPU programming:
  DPU Programming using DOCA
  DPU Programming using P4 DPL
  Introduction to P4-DPDK
  P4-DPDK Security applications

## Slide 39
DPU Labs
DPU cybertraining is supported by NSF Cybertraining program, award #2417823
Lab libraries available to learn about DPU programming:
  DPU Programming using DOCA
  DPU Programming using P4 DPL
  Introduction to P4-DPDK
  P4-DPDK Security applications

## Slide 40
DPU Labs
DPU cybertraining is supported by NSF Cybertraining program, award #2417823
Lab libraries available to learn about DPU programming:
  DPU Programming using DOCA
  DPU Programming using P4 DPL
  Introduction to P4-DPDK
  P4-DPDK Security applications

## Slide 41
DPU Labs
DPU cybertraining is supported by NSF Cybertraining program, award #2417823
Lab libraries available to learn about DPU programming:
  DPU Programming using DOCA
  DPU Programming using P4 DPL
  Introduction to P4-DPDK
  P4-DPDK Security applications

## Slide 42
DPU Workshops
2025 Supercomputing tutorial, Nov 16, St. Louis, MO
2025 Internet2 Technology Exchange (TechEx), Dec 8-12, Denver, CO
Online workshops
More information on workshops and training resources:
https://research.cec.sc.edu/cyberinfra/workshops
https://research.cec.sc.edu/cyberinfra/cybertraining

## Slide 43
Acknowledgements
This work was supported by the U.S. National Science Foundation (NSF), under awards 2417823 and 2346726
The authors would also like to acknowledge the FABRIC team.

## Slide 44
Q&A

## Slide 45
Acknowledgements
In addition to our presenter, we would like to acknowledge the behind-the-scenes team that diligently worked to bring this webinar to production:﻿
KC Wang, content
Chelsea Davis, project manager
Jayasree Jaganatha, social media specialist

## Slide 46
Resources
Connect With Us
Newsletter Signup: bit.ly/FABRICnewsletter
Office Hour Sign Up: bit.ly/FABRIC-Office-Hours
Other Resources
Website: bit.ly/m/FABRICtestbed
YouTube: youtube.com/@fabrictestbed
FABRIC Account: portal.fabric-testbed.net
Ambassador Program: bit.ly/FABRIC-Ambassador-Program
FABRIC LinkedIn: linkedin.com/company/fabrictestbed
Citing FABRIC: bit.ly/citing-fabric
Call to Action
FABRIC Matrix: https://bit.ly/FABRICmatrix

## Slide 47
Thank You for Attending!
Join us for our upcoming webinars:
Date - Stitching Together Innovation with FABRIC Users
Date - Mastering FABRIC: Tips and Tricks Webinar
Visit our YouTube Channel: youtube.com/@fabrictestbed