## Slide 1
Measurement Collection through Custom
Packet Processing in P4
Ali Mazloum, Jorge Crichigno
University of South Carolina
https://research.cec.sc.edu/cyberinfra/
amazloum@email.sc.edu, jcrichigno@cec.sc.edu
IIT Department, University of South Carolina
April 22, 2024

## Slide 2: Agenda
Experimental Topology
System Design
Data Plane
Control Plane
Data Collection and Visualization
Conclusion
2

## Slide 3: Experimental Topology
The topology consists of three servers connected by a P4 programmable switch
Two servers are used to exchange data, and one server operates as the collector
3

## Slide 4: System Design
The data plane is responsible for calculating per-flow the statistics
The control plane periodically triggers the data plane to report the measurements
The data plane utilizes a custom header to append the calculated statistics
The control plane processes and stores the reports received from the data plane of the switch
4
  Measurement calculation
  Measurement reporting
Data Plane
Control Plane
  Periodic triggering
  Measurement collection

## Slide 5: Data Plane
5

## Slide 6: Control Plane
6

## Slide 7: Data Collection and Visualization
7
InfluxDB is used to store the measurements
Grafana is used to query and visualize the measurements

## Slide 8: Conclusion
The system utilizes the data plane to calculate and report per-flow statistics and the control plane to initiate reporting events
Reports are packets with a custom header structure that carry the statistics to the collector
The data plane appends the statistics and the required metadata to the custom headers
Adding a new metric is performed by adding a new header field to the custom header
The control plane of a remote collector extracts the statistics from the headers of the reports
InfluxDB and Grafana are used to store and visualize the measurements
8