## Slide 1
UCF / FLR Workshop on Networking Topics
SDN concepts, Open vSwitch and Open Flow
Jorge Crichigno, Elie Kfoury
University of South Carolina
http://ce.sc.edu/cyberinfra
University of Central Florida (UCF)
Florida LambdaRail (FLR)
The Engagement and Performance Operations Center (EPOC)
Energy Sciences Network (ESnet)
University of South Carolina (USC)
Orlando, Florida
February 17th, 2023

## Slide 2: Agenda
SDN fundamentals – data and control planes
SDN operation
Flow / Forwarding tables
OpenFlow protocol
Limitations of SDN and OpenFlow

## Slide 3: Plane Separation
The first fundamental characteristic of SDN is the separation of planes
  Data plane, implemented in the device
  Control plane, implemented by a centralized controller
Traditional network
W. Stallings, “Foundations of Modern Networking: SDN, NFV, QoE, IoT, and Cloud” Addison Wesley, 2017.
SDN network

## Slide 4: Plane Separation – Data Plane
The data plane implements forwarding functionality (logic and tables for choosing how to deal with incoming packets)
  Forwarding based on MAC address, IP address, VLAN ID, etc.
  Dropping, replicating an incoming packet
Traditional networks
W. Stallings, “Foundations of Modern Networking: SDN, NFV, QoE, IoT, and Cloud” Addison Wesley, 2017.

## Slide 5: Plane Separation – Data Plane
Special-case packets (e.g., routing advertisements) that require processing by the control plane are passed to that plane
Traditional networks
W. Stallings, “Foundations of Modern Networking: SDN, NFV, QoE, IoT, and Cloud” Addison Wesley, 2017.

## Slide 6: Plane Separation – Control Plane
The control plane is moved off the switching device, onto a centralized controller
The algorithms used to program the data plane (populate tables) reside in the control plane (e.g., OSPF, BGP)
Traditional networks
W. Stallings, “Foundations of Modern Networking: SDN, NFV, QoE, IoT, and Cloud” Addison Wesley, 2017.

## Slide 7: SDN Operation
Basic components (bottom-up)
  SDN switches (e.g., Open vSwitch)
  Controller (e.g., ONOS controller)
  Applications (e.g., BGP app, IDS app)
Global view app
BGP app
IDS app
Business app
SDN Controller
Northbound (REST, JSON)
Southbound (OpenFlow)
Control plane
Data plane
Flow table

## Slide 8: SDN Operation – Switches
SDN devices contain forwarding functionality
Forwarding information is stored in flow tables
If it does not find a match, it can either drop the packet or pass it to the controller
Global view app
BGP app
IDS app
Business app
SDN Controller
Northbound (REST, JSON)
Southbound (OpenFlow)
Control plane
Data plane
Flow table

## Slide 9: SDN Operation – Controller
SDN controller implements control plane functionality
It presents an abstraction of the network to the SDN applications running above
It allows the SDN applications to define flows on devices
It maintains a view of the entire network (global network view)
Global view app
BGP app
IDS app
Business app
SDN Controller
Northbound (REST, JSON)
Southbound (OpenFlow)
Control plane
Data plane
Flow table

## Slide 10: SDN Operation – Applications
SDN applications are built on top of the controller
Software applications can implement forwarding, routing, overlay, multipath, access control, etc.
Application are driven by events coming from the controller and from external inputs
Global view app
BGP app
IDS app
Business app
SDN Controller
Northbound (REST, JSON)
Southbound (OpenFlow)
Control plane
Data plane
Flow table

## Slide 11
The interface between the control and data planes has been historically proprietary
Vendor dependence: slow product cycles of vendor equipment, standardization
Forwarding Tables
Legacy network

## Slide 12
In SDN networks, that function is now performed by the controller
  The controller is responsible for programming packet-matching and forwarding rules
Legacy network
SDN network
Forwarding Tables

## Slide 13: Advantages of SDN Networks vs. Legacy Networks
Ease of network management
“More customized” network behavior
Possibility of experimentation and innovation (custom policies, apps can be deployed)
Packets can be forwarded based on other fields, such as TCP port number
Legacy network
SDN network

## Slide 14: Overview of OpenFlow
OpenFlow is a protocol specification that describes the communication between OpenFlow switches and an OpenFlow controller
The consortium responsible for the OpenFlow specification is the Open Networking Foundation (ONF), which was created in 2011
SDN network

## Slide 15: Overview of OpenFlow
A switch receives packets on one port and forward it through another
  Example: port 2 -> port N
Potential actions
  (A) Forward the packet out a local port
  (B) Drop the packet
  (C) Pass the packet to the controller via a PKT_IN message
When the controller has a data packet to
  forward out through the switch, it uses the
  PACKET_OUT message (e.g., route advertisements)

## Slide 16: Overview of OpenFlow
The protocol consists of a set of messages from the controller to the switch and a corresponding set of messages in the opposite direction
Basic ops: defining, modifying, and deleting flows

## Slide 17: Overview of OpenFlow
The secure channel is the path used for communications between the OpenFlow controller and the OpenFlow device
This communication is secured by
TLS-based encryption, though unencrypted
TCP connections are allowed
Connections may be in-band or out-of-band

## Slide 18: Overview of OpenFlow – Flow Table
The flow table lies at the core of the definition of an OpenFlow switch
A flow table consists of flow entries
A flow entry consists of header fields, counters, and actions associated with that entry

## Slide 19: Overview of OpenFlow – Flow Table
The header fields are used as match criteria
The counters are used to track statistics relative to this flow, such as how many packets have been forwarded or dropped for this flow
The actions fields prescribe what to do with a packet matching this entry

## Slide 20: Overview of OpenFlow – Flow Table
The header fields are used as match criteria
The counters are used to track statistics relative to this flow, such as how many packets have been forwarded or dropped for this flow
The actions fields prescribe what to do with a packet matching this entry
Flow table, switch s1

## Slide 21: Overview of OpenFlow
Each message between controller and switch starts with the OpenFlow header
The header specifies the OpenFlow version, message type, message length, and transaction ID of the message
Three categories
  Symmetric: sent by controller or switch w/o solicitation
  Controller-switch: sent by controller to switch
  Async: sent by switch to controller when there is any state change in the system

## Slide 22: Overview of OpenFlow
Example: Controller Programming (populating) Flow Table
At ta, the controller sends a FLOW_MOD (ADD) command
A flow is added for packets entering the switch on any port
  Source IP: 192.168.1.1
  Destination IP: 209.1.2.1
  Source TCP port: 20
  Destination TCP port: 20
  All other match fields have been wildcarded
  The outport port is specified as P

## Slide 23: Overview of OpenFlow
Example: Controller Programming (populating) Flow Table
A packet arrives at the switch through port 2 with source IPv4 192.168.1.1 and destination IPv4 209.1.2.1
The packet-matching function scans the flow table starting at flow entry 0 and finds a match in flow entry F
Flow entry F stipulates that a matching packet should be forwarded out port P

## Slide 24: OpenFlow Additions
The OpenFlow interface started simple, with few protocols that could be matched against incoming packets
Over few years, the specification has been extended with many more header fields and new protocols
Version | Date | Header fields
OpenFlow 1.0 | Dec. 2009 | 12 (Ethernet, TCP, IPv4)
OpenFlow 1.1 | Feb. 2011 | 15 (MPLS, …)
OpenFlow 1.2 | Dec. 2011 | 36 (ARP, ICMP, IPv6, …)
OpenFlow 1.3 | Jun. 2012 | 40
OpenFlow 1.4 | Oct. 2013 | 41
OpenFlow 1.5 | Mar. 2015 | 44
Bossart et al. “P4: Programming Protocol-Independent Packet Processors”
OpenFlow Switch Specs v1.5.1. Online https://tinyurl.com/y4j4a5eh

## Slide 25: Limitations of SDN / OpenFlow
SDN
  Fixed number of header fields
  OpenFlow repeatedly extends the specification
  Long standardization cycles
  Fixed protocols / header fields
  Fixed parser
  Devices still in control of manufacturers
  Operators / programmers limited to functionality specified in the OpenFlow specification
  Match+action stages are in series
P4 switches (see p4.org)
  Operators / programmers can define their own protocols and header fields
  Immediate implementation
  Customized protocols / header fields
  Devices in control of operators / programmers
  Match+action stages are in series or in parallel
  Actions are composed of protocol-independent primitives (switch is not tight to specific protocols)
  More future-proof

## Slide 26: Programmable Switch ASICs
We now have the technology that permits CI engineers to run customized functions
Data Plane
Control Plane
CPU-based control plane
Switch
ASIC
Programmable parser, tables, arithmetic logic
units (ALUs), programmable deparser, …
P4 Code
CI Engineer
compiler
Switch

## Slide 27: Programmable Switch ASICs
We now have the technology that permits CI engineers to run customized functions
  Designed for packet processing operations
Data Plane
Control Plane
CPU-based control plane
Switch
ASIC
Programmable parser, tables, arithmetic logic
units (ALUs), programmable deparser, …
P4 Code
CI Engineer
compiler
Switch

## Slide 28: Programmable Switch ASICs
We now have the technology that permits CI engineers to run customized functions
  Designed for packet processing operations
  Much faster than general-purpose CPUs for processing packets
N. McKeown, “Creating an End-to-End Programming Model for Packet Forwarding,” Netdev 0x14 Conference 2020, https://www.youtube.com/watch?v=fiBuao6YZl0&t=619s.

## Slide 29: Workshop on Networking Topics
Webpage with PowerPoint presentations:
http://ce.sc.edu/cyberinfra/workshop_2023_feb.html
Hands-on sessions: to access labs for the hands-on sessions, use the following link:
https://netlab.cec.sc.edu/
Username: email used for registration
Password: nsf2023