## Slide 1: Researcher / Team Introduction
David W. Matolak
Professor
Department of Electrical Engineering
University of South Carolina
Research Group Overview: Wireless Science & Engineering (WiSE) Lab investigates
Wireless channel characterization: analysis, measurements, simulations, & modeling for variety of environments (terrestrial, air-ground, V2V,…VHF – mmWave (so far!))
Modulation & detection: adaptive PHY, DLL techniques for dependable mobile links, including high-mobility platforms, and low probability of detection (LPD) and anti-jam (AJ) communications
Path 1
Path 2
Path 3
Path 4
Rx
Tx
Aircraft Maintenance Hangar

## Slide 2: NASA University Leadership Initiative Project
Multi-Band Communications & Networking: simultaneously and/or alternately employ different spectral bands for successful transmissions
  Band differences can adjust latency, reduce interference, offload congested bands, improve reliability & resilience to disruption⇒Safer!
Hyper-spectral: HF - VHF - L-band, C-band, K-bands, & mmWave bands
Taxi
Takeoff
Landing
Taxi
En-route
Channel Type 1
Channel Type 2
Channel Type 3
Channel
Type 4
Storm
Channel
Type 5
Ground Site Type 1
Ground Site Type 2
Interferer
(στ2,fD2)
Interferer

## Slide 3: Spectrally-Shaped Filterbank Multicarrier (FBMC)
Over-sea channel
FBMC
LDACS1
Ss-FBMC Transmitter
Ss-FBMC & DME Power Spectra
Ss-FBMC Bit Error Ratio vs. received signal-to-noise ratio
(OFDM)
Design→Lab Tests → Drive Tests→Flight Tests

## Slide 4: Radio Diagram: Ground Station (GS)
2 antennas for each band yields spatial diversity
Single broadband HPA
Multiple RF filters to meet spectral mask, spurious emission suppression

## Slide 5: Radio Diagram: Aircraft
Aircraft=Air Station (AS)
Single antenna for each band
Otherwise design identical to GS

## Slide 6: Radio System: Ground Station
Broadband (700-6000 MHz) HPA, max power 47 dBm
Dual diversity: 2 L-band & 2 C-band GS antennas
  L-band log-periodic antennas w/90-degree HPBW, G=10 dBi
  C-band horn antennas w/60 degree HPBW, G=10 dBi
GS Configuration in Lab

## Slide 7: Terrestrial Drive Test Measurement Sites
At each site had small (~1 km) region around GS where line of sight (LoS) to GS could be maintained
Beyond those small areas, LoS obstructed by trees, buildings, or vehicles
Thus, we measured some good performance, & some outages due to obstructions & multipath propagation
Top Assembly St.; Bottom, Horizon parking garage
Numbered paths 1 & 2 denote car travel path. Insets: GS at each location

## Slide 8: Flight Test Plan: SC Civil Air Patrol (CAP)
CAP’s Gippsland G8 Airvan
Planned flight path for CAP flight tests; from Foreflight © software
Trajectory provided mix of line of sight & below-horizon paths
Relative aircraft to GS orientation varied
Two flights on each of 2 days (4 flights total)

## Slide 9
HPA
Filter (L)
Power
(inverter)
SDRs
RF
Power
(batteries)
Antennas
SC-CAP Flight Test Preparation
Ph.D. student Zeenat Afroze
Team member & pilot Eddie King
Multiple new radio modes tested
GS spatial antenna diversity
Adaptive modulation
Simultaneous L-band & C-band communications
Wideband (5 MHz) C-band transmissions

## Slide 10
NASA ULI: Millimeter Wave (mmWave) Comm.
mmWave systems expanding (e.g., 5G, 6G)
  Offer VERY high data rates, for short range networks
  Require directional antennas
Accurate models of mmWave channels vital for link design
  We measured/modeled in indoor, outdoor, & airport settings in two bands: 30 GHz, 90 GHz
Columbia Metro Airport
Atlanta
Hartsfield

## Slide 11: 90 GHz Measurement Equipment
R&S Signal Generator (Tx), Analyzer (Rx)
Quinstar up/downconverters, amps, horn antennas
attenuators
measured (lab) power spectrum
500 MHz BW, showing multipath distortion effect

## Slide 12
90 GHz Outdoor mmWave Measurements
Outdoor line-of-sight (LOS)-to-non-LOS (NLOS) transition
  Measure increase in attenuation, change in angular direction of strongest signal, & change in delay dispersion
RMS Delay Spread vs. distance into NLOS region (RMS-DS quantifies channel delay dispersion)

## Slide 13
90 GHz LOS to NLOS Transition
Spatial PDP correlation coefficient vs. spatial separation (abscissa) & distance (ordinate) along LOS-to-NLOS transition for Swearingen NW outdoor
For threshold c(Δx,xi)≥0.7
  stationarity distance in NLOS region ranges from 2 cm - 12 cm
The NLOS stationarity distance < LOS stationary distance by factor of more than 100

## Slide 14
Power Delay Profiles for LOS to NLOS Transition
Power delay profiles vs. distance for Swearingen NW outdoor LOS-to-NLOS transition, clockwise from upper left: 0 to 20 cm, 22 to 40 cm, 42 to 60 cm, & 62 to 78 cm
Transition around corner of concrete building
Pedestrian-level antenna heights
Large # multipath components (MPCs) up to 55 cm

## Slide 15
mmWave Measurements at Small Airport: 30 GHz
airport maintenance hangar
Path Loss (dB) vs. distance (m) & fits, mixed LOS/NLOS

## Slide 16: …

## Slide 17: Prior NASA Project: UAS in the NAS
  Explored/ validated technologies for reliable CNPC (C2)
  Medium/large aircraft
  U. South Carolina PHY/MAC
      Air-ground (AG) channel measurements and models
      Radio mod/demod
      Networking

## Slide 18: NASA Air-Ground (AG) Channel Measurements
Simultaneous dual-band 1 x 2 measurements
Seven distinct environments
CIRs for estimating (SIMO)
  Path loss, small-scale fading
  Delay dispersion
  Doppler
  Correlations
Telluride, CO

## Slide 19: NASA: AG Channel Measurements→Models
NASA Glenn Research Center AG channel measurements
  Time-varying channel impulse response (CIR) models for over-water, suburban desert & hilly, mountainous, & near urban
L- and C-bands, ~970 and 5030 MHz
20 m GS antenna height, aircraft altitude ~400 to 1700 m
Downtown
Cleveland
Lake Erie

## Slide 20: Measurement Equipment
DS-SS Stepped Correlator
Dual-Band SIMO
~ 3000 Power Delay Profiles (PDPs)/sec
Band | Signal Bandwidth (MHz) | Frequency Span (MHz) | Maximum Delay Span (μs) | Transmit Power (W) | Tx Amplifier (dB) | Rx LNA Gain (dB) | Cable Loss (dB)
L | 5 | 960-977 | 204.6 | 10 | -- | 15.5 | 4
C | 50 | 5000-5150 | 20.46 | 10 | 7 | 30 | 7.5
Transportable GS with 20 m tower

## Slide 21: Example Measurement Environments
Desert, hilly/suburban, Palmdale, CA, & Lake Erie, 2013
  GC=6 dB, GL=5 dB
  hGS = 20 m
  El/Az beamwidths
    35°/180 ° for C
    60°/120 ° for L
  Aircraft antennas: omni
  monopoles (“blades”)
  Both straight & oval-shaped flight tracks (FTs)
Aircraft view east
Downtown Cleveland
Over 11 GB data (>25 million PDPs) gathered
  Over 42 GB data (>106 million PDPs) gathered

## Slide 22: Large Scale Attenuation: Airframe Shadowing
LOS Blockage: aircraft-specific (S-3B)
  Applicable for similar-sized aircraft
  Shadowing data for all GS environments
Flight path in ECEF coordinates

## Slide 23: Airframe Shadowing (2)
Example shadowing events (PRx vs. t), statistics
Over-Freshwater Statistics |  | C-band |  | L-band | 
 |  | Rx1 | Rx2 | Rx1 | Rx2
Shadow Duration (s) |  | 36.5 | 37.3 | 41.9 | 39.8
Shadow Loss (dB) | Max | 30.4 | 27.5 | 25.5 | 34.4
 | Min | 0 | 4.2 | 2.6 | 5.0
 | Mean | 9.1 | 17.2 | 10.3 | 14.2
 | Median | 6.3 | 16.9 | 9.6 | 12.9
 | Standard Deviation | 7.4 | 6.4 | 4.4 | 5.9
Distance (km) | Max | 21.8 | 21.8 | 21.8 | 21.8
 | Min | 20.5 | 20.5 | 20.1 | 20.3

## Slide 24: Channel Dynamics: Hilly Terrain RMS-DS
RMS-DS vs. distance
RMS-DS “spikes” are not anomalies/noise: they are intermittent MPCs due to terrain, buildings, etc.

## Slide 25: Hilly Terrain PDPs, RMS-DS Statistics
RMS Delay Spread |  | Mean (ns) | Median (ns) | Max (ns) | Standard Deviation (ns)
FT1 | Original | 12.9 | 10.9 | 267.2 | 9.8
 | Moving Averaged, 100 PDPs |  | 11.1 | 87.0 | 6.6
 | Moving Averaged, 1000 PDPs |  | 11.2 | 57.0 | 5.7
FT6 | Original | 35.7 | 10.9 | 995.7 | 55.7
 | Moving Averaged, 100 PDPs |  | 18.6 | 371.8 | 42.9
 | Moving Averaged, 1000 PDPs |  | 19.3 | 349.2 | 40.4

## Slide 26: AG Channel Stationarity Distance Example
Example over-sea SD measured results (Oxnard, CA, FT1)
c(Δx,d)
coll(Δx,d)
LOTS of stats gathered for c & coll
Over-water: median SD(c)~15 m, median SD(coll)~6.4 m

## Slide 27: Over-Sea: Delay Dispersion Example
Looking more closely at RMS-DS & PDPs
PDP#4652
d~1.5 km
MPC
Oval
Straight

## Slide 28: Fresh H2O: Delay Dispersion
Scrutinizing RMS-DS & PDPs
Several large buildings, 3 harbors w/watercraft, water barriers, light houses & oil tanks present
Geometry indicates these obstacles create MPCs
Near-Shore
Reflectors

## Slide 29: …

## Slide 30
Prior Project: Urban Channel Measurements
Collaboration with National Institute of Standards & Technology (NIST)
Urban measurements of path loss & delay dispersion in Denver, CO, with multiple antennas, in multiple frequency bands

## Slide 31
NIST Channel Measurements: Calibration
NIST outdoor test facility, Boulder, CO
Calibrating antennas, transmitter, & receiver in deterministic two-path channel
Used in urban, outdoor, & indoor measurements for Public Safety communications

## Slide 32: …

## Slide 33: New Project: Contested Environment Communications
non-linear chirp spread spectrum
Time-frequency (TF) processing for new adaptive LPD signaling schemes, more sensitive detectors
  TF analysis for spread-spectrum signaling types
  TF geometric processing, extreme-value distribution mapping, Renyi entropy for weak signal ID
LPD for dispersive channels
Game-theoretic analyses for optimal AJ strategies
Noise & ambient signal characterization for LPD
  Wideband measurements of both internal (system) and external (environment) signals, noise & TF representations
f
Signal
spectrum
SC-DS-SS spectrum
MC-DS-SS
spectrum
fc